## Slide 1
EIC Accelerator Physics – Part 1
Sergei Nagaitsev, BNL
CFNS School
6 June 2024
EIC:

## Slide 2: About me – Sergei Nagaitsev
EIC Technical Director, Brookhaven National Lab
Jefferson Lab Professor, ODU Department of Physics (https://fs.wp.odu.edu/snagaits/)
Recent professional experience:
2023 – 2024 EIC Lead Scientist, Jefferson Lab
2018 – 2022 Head of Accelerator Science Programs, Fermilab
2015 – 2022 Professor Part-time, The University of Chicago – Accelerator Physics
2013 – 2018 Chief Accelerator Officer, Fermilab – Accelerator Division
Community service:
2020 Chair, APS DPB
2021 – 2022 Member, HEP Snowmass Study Steering Group

## Slide 3: Outline (Part 1)
Accelerators – engines for discovery
EIC overview
  From an accelerator physicist 
Relevant accelerator physics
  Synchrotrons
  (Brief) beam dynamics
  Phase space, emittance, “beta”
Collider interaction regions
  ”Low-beta” squeeze
Primary
Detector
Location
Future
Detector
Location
Primary
Detector
Location
Future 2nd
Detector
Location

## Slide 4: Engines of Discovery
Physics Today 73, 4, 32 (2020);

## Slide 5: Nobel Prize Accounting: A high-level view on the influence of accelerators on physics
Impact of accelerators on physics was measured through Nobel Prizes:
Criterion: Nobel awardee must have authored document citing accelerator contribution to work
Nobel’s directly influenced by Accelerators by 2009: 24
Average frequency of contribution of accelerators to Nobel in Physics: ~3 years
Count for Nobel Prize-winning researches or discoveries in physics from 1943 to 2009. (Haussecker and Chao, Phys Perspect. 13 (2011), p146)
Reproduced from “The Influence of Accelerator Science on Physics Research,” Haussecker and Chao
Nobel Prize Count

## Slide 6: Accelerators: Engines of Discovery
RHIC
NSLS-II
A DOE User Facility for
Advanced Accelerator &
Laser Research
A DOE User Facility to probe the fundamental
properties of matter, paving the way to new
scientific discoveries and innovations.
A DOE User Facility to probe the
fundamental properties of nuclear matter
and to study what the universe may
have looked like in the first few
moments after its creation.

## Slide 7: Accelerators are instruments for providing beams of charged particles – a highly-directed form of energy – to be used as probes and tools
Projects
Technologies
Science
LHC, EIC,
NSLS-II
Inventions,
development
Discoveries,
research
Vision, concept,
integration,
optimization,
construction
Beams: e-,e+, p, pbar, ions, muons
N ~ 1 to 1014
Particle beams behind physics discoveries
Physics Today 73, 4, 32 (2020)
Core Accelerator Technologies

## Slide 8: Colliders: 31 colliders built since 1959
Center-of-mass energy is ECM= 2E – available for ‘new physics’
7 colliders are in operation today, 2 under construction (EIC and NICA)
- LHC, RHIC, BEPC, Super-KEKB, DAFNE, VEPP-4M, VEPP-2000
April 26, 2024: a joint “Statement of Intent between the United States of America and the European Organization for Nuclear Research (CERN) concerning Future Planning for Large Research Infrastructure Facilities, Advanced Scientific Computing, and Open Science” was signed at The White House.
The SOI expresses an intention by the United States to collaborate on a future FCC Higgs Factory should the CERN Member States determine the project feasible.

## Slide 9: The Scientific Foundation for an EIC was Built Over Two Decades
2002
2007
2009
2013
2015
2018
2010
Gluons and the Quark Sea at High Energies
2012
“…essential accelerator and detector R&D [for EIC] should be given very high priority
in the short term.”
“We recommend the allocation of resources …to lay the foundation for a polarized Electron-Ion Collider…”
“..a new dedicated facility will be essential for answering some of the most central questions.”
“a high-energy high-luminosity polarized EIC [is] the highest priority for new facility construction following the completion of FRIB.”
The science questions that an EIC will answer are central to completing an understanding of atoms as well as being integral to the agenda of nuclear physics today.”
“The quantitative study of matter in this new regime [where abundant gluons dominate] requires a new experimental facility: an Electron Ion Collider..”
Electron-Ion Collider..absolutely central to the nuclear science program of the next decade.
Major Nuclear Physics Facilities for the Next Decade
NSAC
March 14, 2013
2021
Science Requirements and Detector Concepts for the EIC – Drives the requirements of EIC detectors
arXiv:2103.05419
2023
We recommend the expeditious completion of the EIC as the highest priority for facility construction.

## Slide 10: The DOE CD0 Mission-Need 2019

## Slide 11: EIC Project Critical Decisions and Plans
CD-0, Mission Need Approved | December 2019
DOE Site Selection Announced | January 2020
CD-1, Alternative Selection and Cost Range Approved | June 2021
CD-3A, Long-Lead Procurement Approved | March 2024
CD-3B, Long-Lead Procurement Planned Approval | March 2025
CD-2/3, Performance Baseline/Construction Start Plan | End 2025
DOE Independent Project Review for CD-3B and Project Status on Jan 7-9, 2025.

## Slide 12: EIC Requirements
EIC design goals
  High luminosity: L = (0.1-1)∙1034 cm-2 s-1
     10-100 fb-1
  Collisions of highly polarized (>70%) e and p (and light ion) beams
    with flexible bunch by bunch spin patterns
  Large range of CM energies:
    Ecm = 20-140 GeV
  Large range of ion species:
    Protons – Uranium
  Ensure accommodation of a second IR
  Large detector acceptances; good background
    Hadron particle loss
    IR synchrotron radiation backgrounds
“Low”
“High”
uniquely
challenging
Diverse
Unique

## Slide 13: EIC Accelerator Design Overview
Hadron storage ring (HSR): 40-275 GeV (existing)
  up to 1160 bunches, 1A avg beam current (3x RHIC, polarized)
  bright vertical beam emittance (1.5 nm); new vac sleeves
  hadron beam cooling
Electron storage ring (ESR): 5–18 GeV (new)
  up to 1160 polarized bunches
    high polarization by continual reinjection from RCS
  2.5 A avg beam current  9 MW SR power
  superconducting RF cavities
Rapid cycling synchrotron (RCS): 0.4-18 GeV (new)
  2 bunches at 1 Hz; spin transparent due to high periodicity
High luminosity interaction region (new; future 2nd IR)
  L = 1034 cm-2s-1 = 10 kHz-uba, superconducting magnets
  25 mrad crossing angle with crab cavities/crab crossing
  spin rotators (produce longitudinal polarization at IP)
Compare to 50 MW at FCC
Future 2nd
Detector
Location
Primary
Detector
Location
Current 6x NSLS-II

## Slide 14
Notes: LHC design 0.58A p (HL up to 1A), beam-beam parameter 3.4e-4 (3-5—3 HL-LHC)

## Slide 15: Today’s plan
Beam sources
Beam energy
Luminosity
Beam transport (bending and focusing)
Beam size at IP
  Emittance
  ‘beta’ function
Maybe: beam stability

## Slide 16: How to build particle accelerators?
In three easy steps:
One needs particles
Add acceleration
Add focusing
For colliders: add collisions

## Slide 17: Nuclear and Particle Physics
The first “high-energy” accelerator, made by Cockroft and Walton, was immediately used to understand the atomic nucleus. They made the first artificially produced nuclear reaction:
p+Li -> 2He
Early accelerator developments were driven by the quest for higher and higher particle energies, which in turn was driven by developments in nuclear physics (through the 1960s) and then elementary particle physics (1960s-onward)
The largest accelerator is at CERN (LHC). It collides two proton beams of energy 7 TeV each.

## Slide 18: Particle sources
The simplest conceptual model of an electron beam source is a planar diode.
  Cathodes typically operate at 1400K (kT ≈ 0.12 eV)
  An effective work function is about 1.6 eV
Ion sources are generally more complex. The ions are typically extracted from the plasma of a gas discharge.

## Slide 19: Potential-Drop Accelerators
These accelerators use at static, DC, potential difference between two conductors to impart a kinetic energy
+
-
+q
L
E
Earliest particle accelerators were the Cockcroft-Walton generator and the Van de Graaff generator
Highest voltage achieved is 25 MV
It is difficult to establish and maintain a static DC field of 20+ MV
Van de Graff (tandem) generator
Cockroft-Walton generator
100 ft

## Slide 20: Cyclotron (Larmor) frequency
Frequency weakly depends on particle energy (for non-relativistic particles)
Led to invention of a cyclotron

## Slide 21: The Cyclotron Concept
S
N
+
S
+
S
S
The Recipe:
A magnetic field to bend a particle around.
A sinusoidally varying electric field.
Sinusoidal voltage source
E
+
+

## Slide 22: The First Cyclotron
First cyclotron (1931):
1 kV gap voltage
80 kV protons
4.5” in diameter

## Slide 23: Origins of Accelerator Physics Earn Two Nobels
Photo courtesy Lawrence Berkeley Lab
https://history.aip.org/
Nobel 1951
"for their pioneer work on the transmutation of atomic nuclei by artificially accelerated atomic particles."
"for the invention and development of the cyclotron and for results obtained with it, especially with regard to artificial radioactive elements."
Nobel 1939
Two Nobels were awarded for advent of accelerator technologies

## Slide 24: Acceleration by repeated application of time-varying accelerating fields
Two approaches for accelerating with time-varying fields
v
E
E
E
E
v
Circular Accelerators
Use one or a small number of Radio-frequency accelerating cavities and make use of repeated passage through them. This approach is realized in circular accelerators: Cyclotrons, synchrotrons and their variants
Linear Accelerators
Use many accelerating cavities through which the particle beam passes once:
These are linear accelerators

## Slide 25: Beam rigidity
Beam rigidity plays an important role in beam dynamics. For example, the LHC beam is pc = 7 TeV.

## Slide 26: SC dipoles
4.5 K He, NbTi
+ warm iron small He-plant
NbTi cable
cold iron
Al collar
NbTi cable
simple & cheap
NbTi cable
2K He
two bores
4.5T
8.3T
3.5T
5.3T

## Slide 27: EIC Accelerator Design Overview
Hadron storage ring (HSR): 40-275 GeV (existing)
  up to 1160 bunches, 1A avg beam current (3x RHIC, polarized)
  bright vertical beam emittance (1.5 nm); new vac sleeves
  hadron beam cooling
Electron storage ring (ESR): 5–18 GeV (new)
  up to 1160 polarized bunches
    high polarization by continual reinjection from RCS
  2.5 A avg beam current  9 MW SR power
  superconducting RF cavities
Rapid cycling synchrotron (RCS): 0.4-18 GeV (new)
  2 bunches at 1 Hz; spin transparent due to high periodicity
High luminosity interaction region (new; future 2nd IR)
  L = 1034 cm-2s-1 = 10 kHz-uba, superconducting magnets
  25 mrad crossing angle with crab cavities/crab crossing
  spin rotators (produce longitudinal polarization at IP)
Compare to 50 MW at FCC
Future 2nd
Detector
Location
Primary
Detector
Location
Current 6x NSLS-II

## Slide 28
Notes: LHC design 0.58A p (HL up to 1A), beam-beam parameter 3.4e-4 (3-5—3 HL-LHC)

## Slide 29: Luminosity
Interaction rate per unit cross-section
For Gaussian cross-sections

## Slide 30: Paraxial approximation in beams
Linear approximation for all transverse forces.
Ray transfer matrix analysis for beam optics
  Similar to light optics.
Drift space
Thin lens

## Slide 31: Example: electron microscopes
Various axially-symmetric lenses are used in EM’s

## Slide 32: Quadrupoles
Consider examples of lenses:
  Electrostatic quadrupole
  Magnetostatic quadrupole

## Slide 33: Bends (dipole magnets)

## Slide 34: Dipole magnets
-

## Slide 35: Dipole magnets
Thus, for x we obtain
-
-
-
+

## Slide 36: Dipole magnets
For z we have similar
-

## Slide 37: Matrix elements
Drift space:
Harmonic oscillator:

## Slide 38: FODO
Most accelerator lattices (including EIC) are designed in modular ways
  Design and operational clarity, separation of functions
One of the most common modules is a FODO module
  Alternating focusing and defocusing “strong” quadrupoles
  Spaces between are combinations of drifts and dipoles
  Strong quadrupoles dominate the focusing
  Periodicity is one FODO “cell”
  Horizontal beam size largest at centers of focusing quads
  Vertical beam size largest at centers of defocusing quads
By convention horizontal focusing/defocusing is shown; vertical is opposite

## Slide 39
The key is to alternate focusing and defocusing quadrupoles. This is called a FODO lattice (Focus-Drift-Defocus-Drift). :
How To Get Net-Focusing from Quadrupoles???

## Slide 40: Synchrotrons: Periodic Focusing Systems
Periodic focusing systems with periodic boundary conditions
  A long academic history!
  Solid state, quantum mechanics...
Periodic 1D linear focusing system
  Hill’s Equation (homogeneous)
  Overall synchrotron is periodic, as are repeated FODO “cells”
Symmetry is locally broken for “insertions”
  Match boundary conditions between sections with different K values (focusing)

## Slide 41: Phase Space and Emittance
Equations of motion are second-order differential equations
Like classical mechanics, particle trajectories are determined by their equation of motion (Hill’s equation) and two initial conditions
  Horizontal x’,y’ are angles
  Vertical
x’,y’ are small for high-energy accelerators
  Paraxial optics approximations apply
Transverse distributions are usually Gaussian
  RMS distribution ellipse area: emittance [mm-mrad]
Longitudinal similar but different

## Slide 42
Notes: LHC design 0.58A p (HL up to 1A), beam-beam parameter 3.4e-4 (3-5—3 HL-LHC)

## Slide 43: Beta star
Beam size depends on emittance and optics “beta”:
  Look for kinks in beta function plots
beam
magnets
PHYS. REV. ACCEL. BEAMS 23, 041001 (2020)

## Slide 44: Beta in Free Space
Can minimum beam size be achieved in ”free space”
  Yes! We can demonstrate in free space
  Design tensions:
    Low beta* for high luminosity
    Proximity of quadrupoles to IP
    Large-aperture quads feasibility/quality
    (Beam divergence near IP; ”hourglass”)
    (Downstream secondary focus)

## Slide 45: EIC Primary Interaction Region
Different
axis scales!
Existing tunnel and
experiment halls
Focusing (quads)
as close to IP as
possible (~5m!)
Tensions in magnet
requirements:
high field
large apertures
e/p magnet proximity near IP
Chromaticity:
focusing dependence
on particle energy
25 mrad crab crossing
A. Parker (SULI) D. Higinbotham
”Rear side”
”Forward side”