## Slide 1
Hadron Polarization
Frank Rathmann Brookhaven National Laboratory
CFNS Summer School on Physics of the Electron-Ion Collider June 14, 2024
frathmann@bnl.gov

## Slide 2: Outline
Introduction: A Polarized Electron-Ion Collider
Polarized Particle beams
Hadron Polarimetry
Outlook / Summary

## Slide 3
Nuclear Physics A1026 (2022) 122447
wiki.bnl.gov/EPIC/
❶ Emerging Nucleons
How are gluons, sea quarks, and their intrinsic spins distributed in space and momentum in the nucleon?
❷ Nuclear Medium
How do colored quarks and gluons and colorless jets interact with the nuclear medium?
How does the nuclear environment affect quark and gluon distributions?
❸ Gluon Saturation
What happens to the gluon density at high energy?
Are the properties of a saturated gluonic state universal among all nuclei?

## Slide 4: The Electron-Ion Collider
Variable center-of-mass energy:
Ion beams: protons, 3He, , ,
High luminosity:
Polarized electron and proton beams:
Current location of RHIC at Brookhaven National Lab

## Slide 5: The Electron-Ion Collider
Variable center-of-mass energy:
Ion beams: protons, 3He, , ,
High luminosity:
Polarized electron and proton beams:
protons
electrons
Electrons:
Protons:

## Slide 6: The Electron-Ion Collider
Variable center-of-mass energy:
Ion beams: protons, 3He, , ,
High luminosity:
Polarized electron and proton beams:
Electrons:
Protons:
But the energy of polarized protons leaving the source is only 10 keV…

## Slide 7
2. Polarized High Energy Particle Beams

## Slide 8: 1922 Stern-Gerlach experiment
Setup and result of classical Stern-Gerlach experiment
Quantization of new degree of freedom, later called electron spin.
Interpretation was only put forward in 1927, 2 years after Goudsmit and Uhlenbeck found evidence of half-valued electron spin.
Delay attributed to fact that Stern and Gerlach measured size of magnetic moment of Ag atom to be about appropriate for orbital angular momentum .
Factor 2 compensating for factor in spin- particles (“Thomas factor”) was not known at that time.
Experiment showed for the first time the quantization of angular momentum:

## Slide 9
H. Schmidt-Böcking
Otto Stern “Physicist, lateral thinker, Nobel Prize winner”

## Slide 10: The classical Stern-Gerlach experiment
Observation: spatial splitting of Ag atomic beam in inhomogeneous magnetic field.
Classical expectation: The energy of a magnetic dipole (magnetic moment) would produce a continuous energy distribution:
, with force in inhomogeneous field, given by .
  causing a deflection into an upper and a lower Ag spot.
  Quantum-mechanical dipole behaves completely different from a classical one.
Surprisingly, two discrete energy values appeared:

## Slide 11
Magnetic moments and
  Proportionality coefficient: component of in direction of field (“direction of quantization”).
  Unit of measurement is Bohr magneton or nuclear magneton and .
  Magnetic moments belong to electronic spin J or nuclear spin I:
or
In a magnetic field, the energy of the system is proportional to the flux density :
Experimental values for Bohr magneton and nuclear magneton
  Numerical values in terms of and available from NIST http://www.nist.gov/pml/data:
Convention
For positively charged particles and with (e.g., protons) : spin and magnetic moment vectors are parallel.
For negatively charged particles (e.g., electrons) spin and magnetic moment vectors are antiparallel.

## Slide 12
Separation of spin states in inhomogenous fields
The energy of a spin state in a magnetic field is:
Numerical values in terms of and available from NIST http://www.nist.gov/pml/data:
  Classically: or
  Quantum-mechanically:
System with spin in magnetic field splits into components with magnetic quantum numbers .
In case of hydrogen atoms this is the fine-structure Zeeman effect, as observed in the Stern–Gerlach experiment.
Forces acting on the spin components in an inhomogeneous magnetic field are different and depend on the sign of .
Principle of “spin filter” using the spatial separation of spin states.

## Slide 13
Sources of polarized atoms (ions)
For practical applications,
where high beam intensities are desired, Stern-Gerlach arrangement with separation in one dimension is replaced by systems with rotational symmetries, i.e., multipole fields.
Diaphragms eliminate the wrong components and transmit only the wanted states.
Stern-Gerlach filter acts as a nearly perfect polarizer.
of electron spin of atoms in infinitely strong magnetic field ∼ 100 %.
True as long as particle velocities in beam low enough (e.g., thermal), so that magnets separate two spin components completely.
  Widths of partial beams small enough to be separable.
  Widths are a consequence of atoms’ velocity distributions and are a function of beam temperature.
Component with

## Slide 14
Rydberg formula
Fine structure: splitting of spectral lines due to electron spin and relativistic correction to Schrödinger Eq.
Bohr
Fine Structure
Lambshift
Hyperfine
structure
Zeeman effect
Lamb shift: interactions between virtual photons from vacuum energy fluctuations and electron moving around hydrogen nucleus in each of these two orbitals.
Hyperfine structure: arises from energy of nuclear magnetic dipole moment interacting with the magnetic field generated by the electrons.
Zeeman effect: splitting of a spectral line into several components in the presence of a static magnetic field.
Energy levels of the H atom (not to scale!)

## Slide 15
Hyperfine Structure (HFS) of hydrogen (deuterium)
the coupling of the electronic spin with nuclear spin (hydrogen), or (deuterium) to the total angular momentum
, with state vectors .
The eigenvalue equation reads:
, where
(Here, smaller and different terms such as quadrupole interaction in the Hamiltonian of the HFS were neglected)
Using with
it follows that
  Thus, the HFS splitting becomes
The HFS is generated by

## Slide 16
HFS in magnetic field (Zeeman Effect)
.ie., either in a very weak or very strong magnetic field.
We are interested in nuclear polarization, so we preferably expand into
Following the rules of vector coupling, we obtain:
, and
  where especially for :
The total Hamiltonian reads:
For arbitrary magnetic field, one expands into states with “good” quantum numbers:

## Slide 17
Breit-Rabi formula
yields the Breit-Rabi formula
  With
  For practical purposes terms with or are neglected due to the smallness of the nuclear magnetic moment in comparison with the electron magnetic moment.
Parameter is (dimensionless) magnetic field, measured in units of magnetic field corresponding to HFS splitting .
⇒ Allows for universal representations of Zeeman effect of HFS which depend only on spin structure.
Solution of Hamiltonian from previous equation

## Slide 18
HFS of the H Atom
As function of magnetic field parameter for systems with
, and
States are numbered consecutively starting with the highest-energy state.
Zeeman splitting (Breit-Rabi diagrams) of the HFS

## Slide 19
Values of and for H and D atoms
For the three relevant states (shown on slide 14)
Hydrogen | [mT] | [MHz]
1 | 50.7 | 1420
1 | 2.1 | 60
2 | 6.4 | 178
Hydrogen |  | 
 | 50.7 | 1420
 | 2.1 | 60
 | 6.4 | 178
Deuterium | [mT] | [MHz]
1 | 11.7 | 327
1 | 0.5 | 14
2 | 1.5 | 41
Deuterium |  | 
 | 11.7 | 327
 | 0.5 | 14
 | 1.5 | 41

## Slide 20
Calculation of polarization
System with coupled nuclear and electronic spins:
Calculate polarization of each Zeeman component from the Breit-Rabi formular and take weighted average over all occupied components (slide 17).
Field dependent occupation numbers of Zeeman states for calculation of polarization are squares of amplitudes of these states.
Common definitions of polarization:
For H: ,
For D: , and
Symbol ∗ denotes polarization with respect to quantization axis of states:
  e.g., magnetic field direction at ionizer.
  Quantity independent of coordinate system.
  and enter “Figure Of Merit” (FOM) of an experiment.

## Slide 21
Nuclear polarization of H, D in weak and strong fields
 | Hydrogen |  | Deuterium |  |  | 
 | weak B | strong B | weak B |  | strong B | 
state |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  | 1/3 |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  | 0 | 0 | 
6 |  |  |  |  |  | 
 | Hydrogen |  | Deuterium |  |  | 
 | weak B | strong B | weak B |  | strong B | 
state |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  | 1/3 |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  | 0 | 0 | 
6 |  |  |  |  |  | 
Last line shows polarization of atoms in all states focused by the system with electron spin :
  States for H, and
  for D.

## Slide 22
Polarization of Zeeman states of H and D atoms
Polarization of each single Zeeman component of hydrogen and deuterium.
The hyperfine states are numbered as in the figure on slide 18. Field dependent occupation numbers of Zeeman states for calculation of polarization are squares of amplitudes of these states.
The polarization of an ensemble of particles (e.g., in a beam), which are in different Zeeman states is obtained by calculating the weighted average of all occupied components.

## Slide 23
Stern-Gerlach separation of HFS states
In a ground-state atomic beam source:
Separation strength of HFS states is given by force of inhomogeneous magnetic field acting on the “effective magnetic moment”:
  This is defined as the derivative of the energy , given by Breit-Rabi formula (slide 17), with respect to the field strength :
  .
Only for the “pure” components, (see Breit-Rabi diagrams on slide 18), and the separation according to works only for large

## Slide 24
Zeeman separation in multipole magnets
Some comments:
An efficient separation of Zeeman components uses two-dimensional multipole fields with a cylindrical symmetry (quadrupole or sextupole fields).
The principle of a polarized-ion source for use on accelerators was first formulated by Clausnitzer.
In sextupole magnets, lens-like focusing action on spin components of atoms possible, whereas other spin components are defocused.
Optics for magnetic moments of neutral atoms to optimize Stern-Gerlach systems
with features like beam transport, phase space, emittance, acceptance, in analogy to charged-particle optics in electric and magnetic fields.

## Slide 25
Physics and techniques of atomic beam sources (ABS)
Overview
Production of H and D ground-state atomic beams,
Dissociators, beam formation and accomodation,
  RF discharge dissociators
State-separation magnets
RF transitions
Ionizers (not today)
Polarized (gas) targets and storage cells (not today)

## Slide 26
Multipole fields
Historcally, Stern–Gerlach spin-state separation magnet worked only in one dimension:
Much higher atomic intensities are achieved with rotationally symmetric magnetic fields, i.e., by quadrupole and sextupole magnets acting in two dimensions.
Permanent magnets as well as electromagnets (including superconducting magnets) are used in sources.
Nowadays, almost all sources use advantages of modern permanent magnets, so-called “Halbach” magnets.

## Slide 27
Quadrupole and sextupole magnets
 | Quadrupole | Sextupole
Magnetic potential |  | 
Multipole order |  | 
Magnetic potential |  | 
Magnetic field (poletip ) |  | 
Field gradient |  | 
Force | independent of | Proportional to
 | deflection with constant force | harmonic or hyperbolic trajectories
 | Quadrupole | Sextupole
Magnetic potential |  | 
Multipole order |  | 
Magnetic potential |  | 
Field gradient |  | 
Force |  | 
 | deflection with constant force | harmonic or hyperbolic trajectories

## Slide 28
Permanent magnets before 1980
Originally (i.e., prior to 1980), multipole magnets consisted of separate pole-pieces, formed by permanent magnets with high remanence (such as ALNICO V), ending in angular pole-tips from magnetically soft materials (such as soft iron or Vanadium-Permendur).
A soft-iron cylinder provided closing of the magnetic circuit. Typical pole-tip fields that could be reached were about 1 T.
Multipole magnets
Cross-section of a “classical” permanent sextupole magnet of length 25 cm.

## Slide 29
Halbach magnets
New rare-earth magnet material (Nd-Fe-B), developed by Sumitomo Cooperation, Japan:
The new, stronger magnetic materials can be magnetized in arbitrary direction.
Using these materials, new designs of multipole magnets emerged with a number of improvements (∼1980).
  Magnets with smaller surface area and less outgassing were realized.
  Halbach -pole magnets: M segments with changing magnetization.
    after segments, a pole-piece segment with opposite orientation of magnetization appears.
Three different magnetic materials used for ANKE ABS magnets.

## Slide 30
System of sextupole magnets
Poletip field , inner diameter , outer diameter , magnet length , and distance from nozzle.
Presently, permanent magnets provide best way to produce large fields on small diameter.

## Slide 31
Designing a magnet system using tracking calculations
Modern polarized atomic beam sources use four to six separated short sextupoles:
Field strengths and location of magnets determined by tracking calculations, taking into account other requirements:
  overall space constraints, optimum pumping, insertion of RF transition units, etc.
Projection of 3-dimensional trajectories of hydrogen atoms in hyperfine states |1⟩ and |2⟩:
Effective magnetic moment .
Trajectories from nozzle (, ) to target region:
Figure reflects magnet system from slide 30, using pole-tip fields of 1.5 T. Positions and radial dimensions of nozzle, apertures of six magnets, and feeding tube are indicated.

## Slide 32
RF transitions I
Behind a Stern-Gerlach magnet system, still in a strong magnetic field:
Atoms are highly polarized with respect to the spin of valence electrons, but nearly unpolarized with respect to nuclear spin, because magnetic field is highly inhomogeneous, i.e., individual polarizations of atoms point in different directions.
Simply guiding the atoms adiabatically into a region of weak magnetic field, nuclear polarizations of (H) or (D) are achieved (see slide 23).
High nuclear polarization requires changing of the occupation of hyperfine states:
Adiabatic-fast passage method, proposed by Abragam and Winter, induces transitions between different Zeeman hyperfine states.
This technique is employed in all atomic beam sources targets and provides a high nuclear polarization near the theoretical maximum.
Due to magnetic field gradients, the RF transitions are independent of the atom velocity.

## Slide 33
RF transitions II
Beam passes through magnetic field with linear variation of
Resonance at at frequency
Spin with magnetic moment precesses with angular velocity .
Semi-classical picture:
Rotating RF field exerts torque on :
Spin flips from up to down during passage through gradient field.
The rotating field is equivalent to a linear RF field (two counter-rotation fields).

## Slide 34
Classification of RF transitions
RF hyperfine transitions are approximately classified according to the value of the static magnetic field with respect to the critical field :
  Weak-field (WFT): , transition frequencies typically .
  Medium-field (MFT): .
  Strong-field (SFT): , transition frequencies of hundreds MHz to GHz.
Another classification after Ramsey, refers to change of quantum numbers in transitions:
  transitions within one multiplet:
  .
  transitions between different multiplets:

## Slide 35
RF transition frequencies for H and D
WFT and MFT: low- transitions.
WFT: in Zeeman region of HFS where states are nearly equidistant ⇒ multi-quantum transitions within multiplet.
MFT: transitions at higher and RF frequencies ⇒ energies of single-photon transitions in one multiplet sufficiently separated.
SFT: or single-quantum transitions at still higher between single HFS states.

## Slide 36: An Advanced Polarized Proton Source
A. Zelenski et al., J. Phys. Conf. Ser. 295 (2011) 012147
High brightness proton source
Focusing solenoid
Pulsed hydrogen neutralization cell
Superconducting solenoid 30 kG
Pulsed He-ionized cell
Optically pumped Rb cell
Sona shield
Sodium-jet ionizer
Optically Pumped Polarized Ion Source at RHIC:
Current in
Beam polarization at
One proton bunch in RHIC

## Slide 37: Particle Beam Optics
Lorentz Force:
acceleration
experiment
dipole magnets
other magnets
Lattice to keep the particles on a circle.
There is a closed orbit.
Beam has a size and momentum spread.
Particles oscillate around the closed orbit (betatron oscillation).
F0D0 lattice and orbit envelope
Quadrupole magnets focus in one direction only.
Liouville’s theorem: The phase ellipse and the emittance of the beam are invariant.
injection

## Slide 38: Particle Beam Optics
Lorentz Force:
injection
Lattice to keep the particles on a circle.
There is a closed orbit.
Beam has a size and momentum spread.
Particles oscillate around the closed orbit (betatron oscillation).
Periodicity can lead to resonances and beam instability
with integer numbers
orbit
particle trajectory
possible distortion
Optical resonances up to 3rd order
working point
acceleration
experiment
dipole magnets
other magnets

## Slide 39: Particle Beam Optics & Spin
Lorentz Force:
injection
acceleration
experiment
dipole magnets
other magnets
Lattice to keep the particles on a circle.
There is a closed orbit.
Beam has a size and momentum spread.
Particles oscillate around the closed orbit (betatron oscillation).
Periodicity can lead to resonances and beam instability.
The magnetic moment of particles precesses in magnetic fields.
Proton

## Slide 40: Depolarizing Resonances
L.H. Thomas “The kinematics of an electron with an axis.” The London, Edinburgh, and Dublin Philosophical Magazine and Journal of Science 3.13 (1927)
V. Bargmann, L. Michel, and V.L. Telegdi “Precession of the polarization of particles moving in a homogeneous electromagnetic field.” Physical Review Letters 2.10 (1959)
Thomas-BMT equation:
Spin tune is the number of precessions per revolution.
Two types of depolarizing resonances
  Intrinsic resonances
  Imperfection resonances
Resonance strength depends on the local orbit distortion, magnetic field, and crossing speed.
Number of resonances grows linearly with the top energy.
Proton

## Slide 41: Example: COSY
Cooler Synchrotron at FZ Jülich, Germany
Proton accelerator / storage ring
Intrinsic resonances
Imperfection resonances
Momentum (MeV/c)
Momentum (MeV/c)
Working point
Polarization
air quadrupole

## Slide 42: The Relativistic Heavy Ion Collider
“Configuration Manual Polarized Proton Collider at RHIC.” I. Alekseev et al. (2004)
25 GeV
250 GeV
35 keV
200 MeV

## Slide 43: Spin Resonances in RHIC
Imperfection resonances
  integer
Intrinsic resonances
  integer
  Super-periodicity P
  vertical betatron tune

## Slide 44: Resonance Mitigation
Deliberately advance the spin precession to avoid resonance conditions
Group of dipole magnets with alternating horizontal and vertical field directions which rotates the spin vector by 180°
Siberian Snakes: Ya. S. Derbenev, A.M. Kondratenko “Polarization kinematics of particles in storage rings.” Sov. Phys. JETP 37 (1973)
Strong AGS Snake

## Slide 45: Spin Motion through Siberian Snake

## Slide 46: RHIC Proton Polarization
During the first 250 GeV beam operation in 2009

## Slide 47: Spin Motion through a Spin Rotator
Stable spin direction in a circular accelerator is vertical.
Experiments also require longitudinal polarization.
Spin rotators before and after each experiment.
Transverse polarization remnant can cause systematic uncertainties in physics observables.

## Slide 48: Polarized Beams at EIC
Proton beam polarization has to be measured between .
Electron beam polarization has to be measured between .
Each store may be 8 hours long. Possibly shorter?
The beams are bunched and will have alternating polarization states to reduce time-dependent systematic uncertainties.
Bunch spacing is around (close to 1300 bunches in each ring).

## Slide 49: Requirements for Polarimetry
Required:
  Absolute beam polarization
Consider:
  Time-dependence (polarization decay)
  Bunch-by-bunch polarization
  Polarization profile of bunches
  Polarization during ramp (acceleration)
  Polarization vector at experiment
  Physics program includes options beyond (spin ):
    (spin 1) and (spin )

## Slide 50
3. Polarimetry of High Energy Hadron Beams

## Slide 51: Polarization of Particle Bunches
A bunch of particles in vacuum travelling at almost the speed of light
Goes in circles, will be back in about ().
?
For the determination of the polarization, we will have to devise an experiment which is spin-dependent.
Need a representative sample of scattered particles to make conclusive statements about the polarization.
Only a fraction of the scattering probability will depend on the spin:
It is convenient to introduce an asymmetry:

## Slide 52: The Right Frame
left
right
Momentum and spin direction define a coordinate system.
  Longitudinal
  Normal
  Sideways
refers to the projectile
Analyzing power
Polarization
(proton)

## Slide 53: Transverse Single-Spin Asymmetries
Elastic scattering obeys parity conservation and time invariance.
Collision is symmetric (in the center-of-mass frame), recoil and ejectile are indistinguishable.
left
right
ejectile, recoil, projectile, target
For elastic scattering:
(proton)
(proton)
Remember, we just call this

## Slide 54: Elastic Scattering at RHIC energies
Beam momentum is .
Significant analyzing power exists in the Coulomb-Nuclear Interference region.
A. Poblaguev et al., Phys. Rev. D 79, 094014 (2009)
no-flip amplitude:

## Slide 55: Elastic Scattering at RHIC energies
Beam momentum is .
A significant analyzing power exists in the Coulomb-Nuclear Interference region.
Recoil comes out almost perpendicular to the beam direction.
A. Poblaguev et al., Phys. Rev. D 79, 094014 (2009)
Kinetic energy of the recoil proton
Recoil angle

## Slide 56: An Absolute Polarimeter at RHIC / EIC
Polarized atomic hydrogen jet target (HJET)
left
right
scattering plane
(proton)
(proton)
source
Dissociator
RF unit
Holding field
Detectors
beam

## Slide 57: HJET Setup for RHIC / EIC
Polarized atomic hydrogen jet target
Set of eight Hamamatsu strip detectors
12 vertical strips
  pitch
  thick
Uniform dead layer
INNER
OUTER
≈10 cm
75 cm
≈ 0.7 cm
atomic hydrogen target
proton beam
100/250 GeV
Si strip detectors
scattered proton

## Slide 58: Absolute Beam Polarization
❶
Polarization independent background
⇒
❷
Polarization dependent background
background fraction
Background
Background
SIGNAL
SIGNAL
Inclusive
Inclusive
beam
beam
detector
detector

## Slide 59: Measured Beam Polarizations

## Slide 60: Additional Fast Polarimeters
Carbon polarimeters
Fast measurement
Beam polarization profile
Bunch-by-bunch
Polarization decay (time dependence)
Hydrogen jet polarimeter
Polarized target
Continuous operation
per 8 hours of operation
beam
normalization
From our list of requirements:
Time-dependence (polarization decay)
Bunch-by-bunch polarization
Transverse polarization profile of bunches
Also has to be non-destructive!

## Slide 61: Fiber Target Polarimeters
Ultra-thin ribbon targets:
Target holder inside the beam pipe

## Slide 62: From RHIC to EIC
Loss of increased asymmetry at lower energies,
Reduced bunch spacing requires much better understanding of background
  Polarized or unpolarized
  Better: reject/suppress background
  Second detector layer to veto high energy particles
Punch through region

## Slide 63: From RHIC to EIC
Loss of increased asymmetry at lower energies,
Reduced bunch spacing requires much better understanding of background
  Polarized or unpolarized
  Better: reject/suppress background
Increased beam current is problematic for the fiber target
  Very limited cooling (radiation, thermal conductivity)
  Sublimation temperature
  Temperature saturates in a few
Calculation by P. Thieberger, BNL
Can we find a target material that withstands higher temperatures?

## Slide 64
Outlook / Summary

## Slide 65: Requirements and Delivery
 | Polarized HJET | Unpolarized HJET | Carbon polarimeter | Forward neutrons
Absolute beam polarization |  |  |  | 
Polarization decay |  |  |  | 
Transverse profile |  |  |  | 
Longitudinal profile |  |  |  | 
Polarization vector |  |  |  | 
Bunch polarization |  |  |  | 
(*) Increased systematics
(*) can be calculated, but needs to be confirmed; full background subtraction
(*) depends on the target
(*) limited space for detectors with current magnet configuration
(*) less accurate than pC

## Slide 66: Recap: Hadron Polarimetry
Proton beam energies:
Combination of devices for
  Non-destructive
  Absolute polarization
  Fast measurements during store
  Bunch profile
  Local polarimetry at experiment
Potential for future polarized light ion beams
  Location allows for upgrades to the polarimeter setup

## Slide 67: A Polarized Electron-Ion Collider
The EIC will be the first dedicated polarized electron-ion collider.
Polarimetry is an integral part of the collider design to meet the demands of the physics goals.