## Slide 1: Running conditions and staging for EIC
E.C. Aschenauer (BNL)
Co-Associate Directors for the Experimental Program
Exotic heavy meson spectroscopy and structure with EIC
April 14 - 17, 2025

## Slide 2
What we are building

## Slide 3: EIC Design Overview
Based on existing, well maintained, well performing RHIC
Hadron Storage Ring (RHIC Rings) 40, 100-275 GeV
  Superconducting magnets (existing)
  1160 bunches, 1A beam current (3x RHIC)
  Bright vertical beam emittance 1.5 nm (“flat beams”)
  Strong cooling (coherent electron cooling)
Electron Storage Ring 5–18 GeV
  Large beam current, 2.5 A, 9 MW S.R. power, S.C. RF
  Need to inject polarized bunches
  Swap-out injection for electron bunches (at 1 Hz) to maintain high polarization
Electron rapid cycling synchrotron, 1Hz, 0.4 -> 18 GeV
  Spin transparent due to high quasi-periodicity
High luminosity Interaction Region(s)
  Large bore superconducting final focusing magnets
  25 mrad crossing angle with crab cavities
  Spin Rotators (longitudinal spin)
  Forward hadron instrumentation
  Bunch Crossing ~ 10.2 ns/98.5 MHz
RHIC
US-EIC:
polarization, ion species together with its luminosity and √s coverage makes it a completely unique machine world-wide.

## Slide 4: Thoughts on Polarization
Science Requirement for Polarisation:
need high polarization (~70%)  experimental uncertainties proportional to 1/(Pe2PA2L) or 1/(Pe/A2L) depending on measurements (single or double spin dependent observables)
if electron polarization is required, it needs to be always longitudinal  requires ESR spin rotators
to limit systematics  optimum would be to have arbitrary spin patters for both HSR and ESR
HSR: have trains of 4 bunches with the same spin direction​
ESR: using RCS allows for arbitrary spin patters in the ESR through replacements
Up polarization state for electrons gets depolarized due to Sokolov Ternov
 Swap-out injection for electron bunches (at 1 Hz) to maintain high polarization
Maximum replacement times (= max. allowable storage times in ESR) are based
on 85% injected polarization and 70% time averaged polarization

## Slide 5: Beam Background
Background/radiation sources : Different to hadron-hadron colliders beam related
background cross-sections are larger than signal cross-section
Proton Beam
  Low beam lifetime during injection and ramping
  beam gas event: hadron beam interacts with rest-gas
Electron Beam
  background due to de-excitation of beam if bunches are replaced
  Touschek losses
  losses due to Colomb Scattering
  electron beam gas events due to Bethe Heitler process eBeam + H2restgas  e’ + g + H2restgas
  a good vacuum is critical
   impact on SR, after 10000 Ah correspond to 5 month @ 1034 cm2s-1 5 x 10-9 mbar
  synchrotron radiation
  It is critical to keep the dipole strength closes to the IP low, SR mask design and gold coating
  of Be-section of beam pipe
GEANT4
DIS ep: 18 GeV x 275 GeV Luminosity: 1.54x10³³ cm²s⁻¹.
Electron Beam Gas 10 GeV vacuum after 10000 Ah
Hadron Beam Gas 275 GeV vacuum after 10000 Ah
At 18 GeV @ 0.2A:
~ 1GHz

## Slide 6
Lessons from recent other colliders

## Slide 7: Experience ramping up KEKB and SuperKEKB
KEKB took ~5 years to reach design luminosity
SuperKEKB has not yet reached design luminosity
> 20 below goal
operating since 2019
Several reasons, beam instabilities and beam backgrounds

## Slide 8: Lessons from HERA II upgrade
HERA performed an upgrade to increase luminosity by a factor of 5
  Mainly by squeezing the beam more at the IP by redesign of the IR
The upgrade increased backgrounds dramatically  Several month shutdown to implement improvements
Electron beam polarization never reached HERA-I levels, H1 and Zeus solenoids (~1T) not well compensated
Main culprits:
  no careful simulations prior to the upgrade
  Proton beam-gas interactions most severe background
    Needed an extremely good vacuum to mitigate this
  Synchrotron radiation background
    Background to detectors
    Excess heating of beam pipe
      Can damage flanges, etc.
      Can heat beam pipe, decreasing vacuum
  Electron beam-gas

## Slide 9: Lessons from HERA II upgrade
Dynamic pressure increase due
to thermal and photo desorption
Pressure vs. integrated electron
current 2002 - 03
Proton Beam Gas Background
Two time constants for vacuum
conditioning
Short term after leaks 20 – 30 days
Long term 600 days

## Slide 10: Lessons from HERA II upgrade
Electron polarization through Sokolov Ternov
Luminosity and Polarization have been strongly anti-corelated

## Slide 11: Lessons learnt from pp Colliders
Tevatron
LHC
RHIC
The pbar electron cooler was added in July of 2005. The initial luminosity increased by ~50% at first and then it took many years to take advantage of the cooler by optimizing the store length, beam-beam interactions, etc.
First Beam in 2000
Polarization and Luminosity often anti-corelated.
Took in 2015 in one year the integrated luminosity from all the years before at √s=100 GeV and for √s=250 GeV in 2017
First beam September 10th, 2008, malfunction 9 days later no beam for experiments till 2010, March 19th, 2010 collisions at 7 TeV
Design Lumi was reached June 2016
13.6 TeV reached April 2022

## Slide 12
Status of EIC Project

## Slide 13: DOE EIC Critical Decision Milestones & Risks
2019
2021
CD-3A, Long Lead Procurement, approved March 2024. Excellent use of IRA funding.
CD-3B, Long Lead Procurement, approval planned for March 2025.
CD-2, Project Performance Baseline, requires a more certain annual funding profile.
CD-2/3C, Performance Baseline, Q2FY26
CD-3, Construction Start, Q1FY27✽
CD-4 early finish: Q4 2033
CD-4 = Q1 2036
✽ FY25 and FY26 funding will impact CD-2 and CD-3 milestone dates.
Notes: CD-2, Project Performance Baseline, requires an annual funding profile.

## Slide 14: CD-3A status
Accelerator
Detector
Infrastructure
~$90M

## Slide 15: CD-3B Overview
The EIC Project requested authority to execute ~ $53M in LLPs, including 35% contingency during CD-3B-review January 2025.
Electron Storage Ring (ESR) Dipole Magnets
Advanced Photon Source (APS) Sextupole Magnet Refurbishment, Testing, and Measurement
ESR Magnetic Measurement Bench
APS Quadrupole Magnet Refurbishment, Testing and Measurement
ESR APS Quadrupole Magnetic Measurement Stand
* Lead Tungstate Crystals for the Detector Backward Electro-Magnetic (EM) Calorimeter - Batch 3 and Batch 4
* Scintillating Fibers for the Detector Barrel - Bath 2 and Forward - Batch 2 EM Calorimeters
* Steel for the Detector Forward Hadronic Calorimeter
Detector Solenoid Magnet Power Supply
Detector Electronics Versatile Link Plus Transceiver (VRTX+) and low Power Giga-bit transceiver (1pGBT)
Detector Endcap Structures – Flux Return Steel
Accelerator
Detector
* Continuation of CD-3A contracts

## Slide 16: EIC Project CD-2 Planning
CD-2 Project Planning Objectives and Constraints:
Scope required for the DOE Project Key Performance Parameters (KPPs)
Develop plans for the execution of the portfolio of “off-project” scope
EIC Project total cost less than $3B (working to optimize scope within this objective)
DOE annual project funding not to exceed $300M per year
EIC construction start following the conclusion of RHIC operations
Start Science Program when electron-ion collisions begin!
The constraints result in a longer construction schedule and “dark period” than desirable. This can be partially mitigated by constructing EIC in two stages:
Start of Science Program: Electron-ion collisions with the ePIC detector
Mission Need: Additional project scope required to meet the Mission Need
One integrated project delivery plan for the EIC aligned with annual funding constraints.

## Slide 17: Preparation for CD-2 and CD-3 w/ Subprojects
Requirements
EIC is a single, integrated line-item project.
Subprojects will have well-defined deliverables and interfaces.
Completed subprojects will enable the start of the EIC “early science program.”
Annual funding profile for the subprojects must be consistent with DOE guidance.
Potential EIC Subprojects:
Subproject 1: Hadron storage ring modifications, electron storage ring, and infrastructure
Subproject 2: IR integration, IR superconducting magnets, ePIC detector
Subproject 3: Electron injector systems and related infrastructure
Start Science Program
Subproject 4: RF power, 41 GeV by-pass, 18 GeV capability

## Slide 18: EIC and Subprojects
Subproject 1 - Accelerator – HSR, ESR, INF |  |  |  |  |  | 
 | Subproject 2 - IR Integration, SC Magnets, Detector |  |  |  |  | 
 |  | Subproject 3 - Electron Injector, Infrastructure |  |  |  | 
 |  |  | Subproject 4 - Full EIC Capabilities |  |  | 
Science Program starts after Subproject 3 is complete.
TIME

## Slide 19
Ramping up EIC performance

## Slide 20: EIC NAS Science Pillars
The EIC will unravel the different contribution from the quarks, gluons and orbital angular momentum
SPIN is one of the fundamental properties of matter.
All elementary particles, but the Higgs carry spin.
Spin cannot be explained by a static picture of the proton
It is the interplay between the intrinsic properties and interactions of quarks and gluons
How can we understand their dynamical origin in QCD?
What is the relation to Confinement
How are the quarks and gluon distributed in space and momentum inside the nucleon & nuclei?
How do the nucleon properties emerge from them and their interactions?
Does the mass of visible matter emerge from quark-gluon interactions?
Atom: Binding/Mass =
0.00000001
Nucleus: Binding/Mass =
0.01
Proton: Binding/Mass =
100
For the proton the EIC will determine an important term contributing to the proton mass, the so-called “QCD trace anomaly
How do the confined hadronic states emerge from quarks and gluons?
Is the structure of a free and bound nucleon the same?
How do quarks and gluons, interact with a nuclear medium?
How do the quark-gluon interactions create nuclear binding?
What happens to the gluon density in nuclei? Does it saturate at high energy?
How many gluons can fit in a proton?
How does a dense nuclear environment affect the quarks and gluons, their correlations, and their interactions?
?
=
gluon
splitting
gluon
recombination

## Slide 21: Accelerator at Day One and Ultimate
RCS:
7nC / bunch Add an accumulation ring to reach 28 nC / bunch
5 – 10 GeV polarized e- and add RF to accelerate to 18 GeV electrons
HSR:
100 – 250 GeV polarized p Update PS to reach 275 GeV protons and 110 GeV/u nuclei
100 GeV/u nuclear beams add 41 GeV bypass to get full HSR beam energy capabilities
cooling at injection energy
Proposal for the Day-One Physics and the initial years of science is driven by
  Start of the promised NSAC/NAS science program
  Alignment with expected order in commissioning the collider and ramp up of performance that comes with gain of operational experience
  Having access to new physics results early to get high impact publications, i.e. PRLs, ……
ESR:
7nC / bunch Add more RF cavities to operate at 18 GeV electrons
5 – 10 GeV polarized e- and 28 nC / bunch
Early Science Program
Full EIC Capabilities

## Slide 22: Accelerator Performance for NAS Science
map the out nucleon and nuclei structure from high to low x
span center-of-mass energy √s: 45 – 100 GeV
wide center-of-mass energy: √s: 30 – 140 GeV
access to spin structure of nucleons and nuclei
Spin vehicle to access the spatial and momentum structure of the nucleon in 3d
quark – gluon structure of light nuclei
polarized electron and hadron (p, He-3) beams
accessing the highest gluon densities  saturation
How quarks and gluons interact with a nuclear medium
nuclear beams: d to Pb at √s: 45 – 63 GeV
nuclear beams: d to Pb at √s: 30 – 90 GeV  access to highest & lowest x
mapping the spatial and momentum structure of nucleons and nuclei in 3d
high luminosity ≤1033 cm-2s-1
large acceptance in pT (0.2 – 1.3 GeV) through forward focusing IR magnets
access to rare probes, i.e. Ws and BSM Physics
precision mapping the spatial and momentum structure of nucleons and nuclei in 3d
high luminosity: > 1033 cm-2s-1
gluon emission
?
=
gluon recombination
EIC Mission Need
& Early science program
Full EIC capabilities

## Slide 23: What will be installed for the early science program
Dipoles
Zero Degree
Calorimeter
Off Momentum
Detectors
Roman
Pots
Far Forward
SC Magnets
B0 Magnets
& Detectors
Rear
SC Magnets
Low Q2
Taggers
pC Hadron
Polarimeter
Luminosity
Monitor
Photon
Beam
Hadron Storage Ring
Electron Storage Ring
Ring Inside
Ring Outside
Electrons
Hadrons
Goal:
central ePIC has all subsystems installed
Ancillary detectors all supports are installed, but some of the detector packages are not installed for safety reason for year 1.
ZDC and Lumi-detector are fully installed
Off-Momentum detectors should be in save position, so they can be used if beam is stable
Roman Pots will not be installed
low Q2 Tagger should be discussed
hadron and electron polarimetry will be installed from day-1 operating EIC

## Slide 24: What do we need to commission
RCS:
  operate the RCS
  get polarization in the RCS
  swap out of electron bunches in the ESR
ESR:
  operating with spin rotator to get longitudinal polarization
  swap out of electron bunches to preserve polarization, needed because Sokolov Ternov depolarizes ”up” spin direction
HSR:
  operating beams off center
  transverse and longitudinal beam polarization (needs spin rotator) for protons and He-3
  pre-cooling of hadron beams
  operating with crab cavities
Maximum replacement times (= max. allowable storage times in ESR) are based
on 85% injected polarization and 70% time averaged polarization

## Slide 25: Beam Energy and Average Orbit Radius in the HSR
Since the electron revolution frequency is fixed, the hadron orbit must be adjusted with energy to keep the collisions in sync.
70 mm beam pipe
20 mm
275 GeV
100 GeV
store
130 GeV
U
Au,
p
Zr
Ru
Cu
d
3He
p
Prefer ~130 GeV/u, which corresponds to a ‘centered’ hadron beam (path length difference DR ~ 0, this is achieved for a beam where Z ~ 0.5A)  Ru, Cu, Ag, …..
Do not want to exceed the present RHIC maximum dipole fields (corresponds to 250 GeV protons or 833 T-m)

## Slide 26: EIC Science Program in the early Years of EIC
Proposal to bring EIC online got feedback from
ePIC Leadership June 2024
Detector Advisory Committee Meeting June 2024
Users during EIC-UG/ePIC Summer Meeting July 2024
EIC Project Strategy Workshop August 2024
EIC@JLab Friday meeting September 2024
ePIC dedicated meeting on early science September 2024
Machine Advisory Committee Meeting September 2024
EIC CD-3B and Status Directors review October 2024
EIC RRB Meeting November 2024
EIC DOE OPA CD-3B LLP Review January 2025

## Slide 27: Proposal for EIC Science Program in the First Years
Year - 1
Start with Phase 1 EIC
New Capability:
Commission electron polarization in parallel
Run:
10 GeV electrons on 115 GeV/u heavy ion beams (Ru or Cu)
Physics:
Add your preferred science topic
Year - 2
Phase 1 EIC
+ long. electron polarization
New Capability:
Commission proton polarization in parallel
Run:
10 GeV long. polarized electrons on 130 GeV/u Deuterium
Physics:
Add your preferred science topic
Run:
Last weeks 10 GeV long. polarized electrons and 130 GeV polarized protons
Physics:
Add your preferred science topic
Year - 3
Phase 1 EIC
+ long. electron polarization
+ proton polarization
New Capability:
Commission running with hadron spin rotators
Run:
10 GeV long. polarized electrons on 130 GeV transverse polarized protons
Physics:
Add your preferred science topic
Run:
Last weeks switch to longitudinal proton polarization
Physics:
Add your preferred science topic
Year - 4
Phase 1 EIC
+ long. electron polarization
+ proton polarization
+ operation of hadron spin rotators
New Capability:
Commission hadron accelerator to operate with not centered orbits
Run:
10 GeV long. polarized electrons on 100 GeV Au
Physics:
Add your preferred science topic
Run:
10 GeV long. polarized electrons on 250 GeV transverse and longitudinal polarized protons
Physics:
Add your preferred science topic
Year - 5
Phase 1 EIC
+ long. electron polarization
+ proton polarization
+ operation of hadron spin rotators
+ operation of hadron beams with not centered orbits
Run:
10 GeV long. polarized electrons on 100 GeV Au
Physics:
Add your preferred science topic
Run:
10 GeV long. polarized electrons on 166 GeV transverse and longitudinal polarized He-3
Physics:
Add your preferred science topic
Time to install additional ESR RF and HSR PS to
reach design Current and max. Energies

## Slide 28: Proposal for EIC Science Program in the First Years
Year - 5
Year - 6
Year - 7
Phase 1 EIC
+ long. electron polarization
+ proton polarization
+ operation of hadron spin rotators
+ operation of hadron beams with not centered orbits
New Capability:
Commission ESR & HSR at max. energy and beam currents
Run:
18 GeV long. polarized electrons on 275 GeV/u polarized (longitudinal & transverse) proton beams
Physics:
Add your preferred science topic
Phase 1 EIC
+ long. electron polarization
+ proton polarization
+ operation of hadron spin rotators
+ operation of hadron beams with not centered orbits
+ operation of ESR & HSR at max. energy and beam currents
New Capability:
Operate HSR with 41 GeV bypass
Run:
5 GeV long. polarized electrons on 41 GeV transverse polarized proton beams
Physics:
Add your preferred science topic
Phase 1 EIC
+ long. electron polarization
+ proton polarization
+ operation of hadron spin rotators
+ operation of hadron beams with not centered orbits
Run:
10 GeV polarized electrons on 100 GeV Au
Physics:
Add your preferred science topic
Run:
10 GeV long. electrons on 166 GeV transverse and longitudinal polarized He-3
Physics:
Add your preferred science topic

## Slide 29: Assumptions and Luminosity Calculation
7 nC electron bunch charge compared to 28 nC (CDR)
Constant proton beam IP divergencies are maintained throughout the store by gradual increase of proton IP beta-functions as the beam emittance increases.
The electron IP beta-functions are adjusted accordingly to match electron and proton transverse beam size.
Ion beam is cooled at low energy (24 GeV/u) but no stochastic cooling is used in the store
1 Run is ½ year operation at 80% uptime
2 h store turnaround time
30 min at the beginning of the store is taken by the ESR fill and detector turn-on
Not yet included a ramp of of luminosity through the Run
 at RHIC: 1st week 25% of projected lumi / week
2nd week 50% of projected lumi / week
3rd week 75% of projected lumi / week
4th week to X week 100% of projected lumi / week
 First guess for EIC early years
1st week 10% of projected lumi of the run / week
increase by 10% every  10 weeks to reach projected lumi / week

## Slide 30: Assumptions and Luminosity
 | Lumi per Fill (5 h) | Lumi per Year
10 GeV e x 115 GeV Ru | 1.3 pb-1 | 0.9 fb-1
10 GeV e x 100 GeV Au | 1.2 pb-1 | 0.84 fb-1
10 GeV e x 130 GeV d | 16 pb-1 | 11.4 fb-1
10 GeV e x 166 GeV 3He | 12 pb-1 | 8.65 fb-1
Note:
eA luminosity is per nucleon
eA luminosities for Phase-I
Possible Beam energies:
electron: 5 GeV, 10 GeV and ultimately 18 GeV
proton: 41 GeV, 100 GeV to 255 GeV ultimately 275 GeV
Au: 41 GeV, 100 GeV to 110 GeV ultimately
A: 41 GeV, 100 GeV to Max ~255 / (A/Z) ultimately ~275 / (A/Z)

## Slide 31: ep Luminosity for Phase-1
High Divergence | Lumi per Fill (5 h) | Lumi per Year
5 GeV e x 250 GeV p | 9.26 pb-1 | 6.48 fb-1
10 GeV e x 250 GeV p | 13.12 pb-1 | 9.18 fb-1
5 GeV e x 130 GeV p | 6.3 pb-1 | 4.36 fb-1
10 GeV e x 130 GeV p | 7.6 pb-1 | 5.33 fb-1
Low Divergence | Lumi per Fill (5 h) | Lumi per Year
5 GeV e x 250 GeV p | 6.81 pb-1 | 4.78 fb-1
10 GeV e x 250 GeV p | 8.8 pb-1 | 6.19 fb-1
5 GeV e x 130 GeV p | 5.8 pb-1 | 4.1 fb-1
10 GeV e x 130 GeV p | 7.1 pb-1 | 4.95 fb-1
Remember:
high divergence: higher lumi, but reduced acceptance
for low forward particle pTmin
low divergence: lower lumi, but increased acceptance
for low forward particle pTmin
 important for exclusive processes
Low-divergence
Illustration
Compare to HERA integrated luminosity 1992 – 2007: 0.6 fb-1

## Slide 32: Luminosity ep for Phase-1
Compare to HERA peak luminosity
of 5x1031cm-2sec-1
Max average luminosity without SHC: 0.8 x 1033 cm-2 s-1 with 5.9 hr store
250 GeV x 10 GeV