## Slide 1: Machine Learning Applications for Improving Accelerator Operations for the EIC
Probing the frontiers of nuclear physics with AI at the EIC (II)
Mar 21, 2025
Weijian (Lucy) Lin
PI: Kevin Brown

## Slide 2
Motivation
Particle accelerator – kilometer-scale machine with thousands of coupled components to generate and preserve beam with very precisely defined qualities (e.g., energy, emittance, luminosity etc.)
Traditionally maintained with many hours of manual tuning, taking time away from data collection
Constantly varying complex system – no constant set of routine, needs real-time adjustments

## Slide 3
Alternating Gradient Synchrotron (AGS) and its Booster serve as part of the injector compound for RHIC and future EIC
Motivation
 | Max Energy [GeV] | Pol. At Max Energy [%]
Source+Linac | 1.1 | 82-84
Booster | 2.5 | ~80-84
AGS | 23.8 | 67-70
RHIC | 255 | 55-60
Loss in polarization along the chain
Difficulty in improving beam quality:
polarimeter measurement is slow and has big error bars
tuning involves many control parameters and is mostly done by hand
Machine Learning (ML) techniques can be used to optimize beam luminosity, quality, and polarization in RHIC and EIC

## Slide 4
Improve Operations with ML
Figure-of-merits (FOM) for ML algorithms (“experimental outputs”): emittance, beam intensity, polarization
Possible areas where ML is useful:
  Cooling optimization
  Injection optimization
  Digital-twin & Error detection
  Electronic Logbook upgrade
Useful ML methods:
  Bayesian Optimization (BO)
  Neural Network (NN)
  Reinforcement Learning (RL)
  Natural Language Processing (NLP)

## Slide 5: Cooling Optimization

## Slide 6: Low Energy RHIC electron Cooling (LEReC)
LEReC is used to increase the luminosity, it was successfully improved the luminosity in 2020 and 2021 runs
704 MHz e-bunches are created in the 400 keV Cornell gun, and delivered to the cooling sections (20 meter), where they co-travel with ion bunches
 The new EIC pre-cooler layout follows the same principle, profiting form the same ML techniques
Cornell DC Gun

## Slide 7: LEReC experiment settings
Only the first 4 BPMs are considered due to limited machine time
Cooling rate:
Ions are assumed in the center position (x=0, y=0)
Goal: use Bayesian optimization (BO) to maximize by aligning electron orbit with ion orbit

## Slide 8: LEReC experiment results
Bayesian optimization algorithm trained with 40 initial samples to optimize transverse cooling rate
The system reaches optimal status when cooling rate balances the IBS-driven growth rate, so approaches 0 once the system reaches equilibrium
Algorithm converged quickly (reach close neighborhood in 3 steps)
Tune electrons from the farthest positions to the center and maintain the trajectories
Avg. Number = 15
equilibrium

## Slide 9: Coherent electron Cooling
Designed to cool 26.5 GeV/u ion beam circulating in RHIC’s yellow ring.
CeC CW SRF accelerator with unique SRF electron gun generates electron beams with quality sufficient for the current experiment and for the future EIC cooler
Time-resolved diagnostics beamline is used to provide high precision measurements of electron beam quality

## Slide 10: Quadrupole scan with two quads
Scan two quads (Q3, Q4) with opposite polarity keep beam focused vertically
Find quad combination settings that gives best vertical focusing
Find best Q3-Q4 combinations with sequential scans: 1) scan 13 Q3 settings; 2) for each Q3 setting, scan 9 Q4 settings
Time taken: ~ 5 minutes for each Q3 setting, > 1 hour for an entire scan routine

## Slide 11: Speed up quad scan with Neural Network
Time consuming sequential scans
Train a ML model to establish mapping between quadrupole settings and beam size
Trained ML model predicts best Q3-Q4 combinations without additional scans
Useful for faster general beam tuning & as starting point of optimization
Artificial Neural Network
Desired beam properties
Quadrupole (or other tunable) settings

## Slide 12
Trained NN accuracy on 54 data points: 93.65%
Tested 7 proposed Q3-Q4 combo settings
Obtained Y RMS values around 0.3 – 0.4 mm range: satisfactory preliminary results
Successfully cut scan time by 50%
First 6 rounds: 54 saved data points
Remaining 7 rounds: 7 data points using Q3-Q4 settings predicted by NN model
New CeC routine test results

## Slide 13: Injection Optimization

## Slide 14: Booter injection
From Linac
bend
To Booster
Booster injection process sets maximum beam brightness for rest of acceleration through RHIC
Known emittance effect on polarization loss
Intentional horizontal and vertical scraping reduce emittance to RHIC requirements
Goal: minimize emittance / maximize beam intensity after scraping
Controls: Linac to Booster (LtB) transfer line optics
Method: Bayesian optimization (BO)
scrape

## Slide 15: LtB controls and measurement
13 quadrupoles and 16 correctors between Linac and Booster
Common practice to improve Booster injection efficiency: tune last few correctors at the end of the LtB line
Criteria to check injection efficiency: Booster early and late intensity
Booster

## Slide 16: LtB optimization: 2 correctors + 2 quadrupoles
Controls: Power supply currents of two correctors and two quadrupoles at the end of the LtB line
Beam size decrease in both planes in the BtA line in correspondence with intensity increase

## Slide 17: Electron Beam Ion Source
Heavy ion source to replace Tandem as pre-injector for RHIC
 |  | Injection [fc96] | Extraction [xf14]
1 | IonLens20-40kV |  | 
2 | DeflPlatBias |  | 
3 | 16PoleX |  | 
4 | 16PoleY |  | 
5 | Gridded_Lens |  | 
6 | Horiz_Bend_Defl |  | 
7 | Inter_Vert_Defl |  | 
8 | Inter_Vert_Defl_Lower |  | 
9 | Horiz_Sphere_Bend |  | ×
10 | RFQ_Horiz_Bend | × | 
11 | LEBT_Solenoid | × | 
 | Total Variables | 9 | 10
LION
EBIS Injection Line (fc96)
EBIS
EBIS Extraction line (xf14)
RFQ
MEBT
Linac
HEBT

## Slide 18: EBIS extraction line optimization
1.4
~2.0
~43% improvement after optimization
10 control parameters measured at xf14 were used to maximize ion beam intensity
Objective is average intensity over 4 super-cycles (6.6 sec per cycle), multiplied by a negative scaling factor, BO algorithm aims to minimize objective
43% improvement observed after 60 iteration (~57 minutes)
Objective
xf14 intensity

## Slide 19: AGS injection
Extraction septum at F6 in Booster, injection septum at L20 in AGS, no scraping
Multi-wires MW006, MW060, MW125, MW166
Emittance measured by AGS Ionization Profile Monitor (IPM)
Goal: maximize beam brightness in the AGS
Controls: Booster to AGS (BtA) transfer line optics

## Slide 20: BtA optimization: 4 correctors
Controls: Power supply currents of two vertical and two horizontal correctors.
Target: Increase brightness. Increase intensity and decrease beam size.
Method: Ruin initial settings, use Bayesian optimization to re-optimize settings.
Results: Automatically achieved previous maximum brightness and intensity in iterations with new settings

## Slide 21: Digital-twin and Error detection

## Slide 22: Orbit responses measurement script
Script development with Collider Accelerator Department (CAD) Controls Group
Can be easily adapted to other accelerators at BNL
Script sets three corrector settings: positive, zero, negative; and save corresponding orbits
All magnet settings (including dipoles and quadrupoles etc.) are saved for model calibration for digital-twin

## Slide 23: Orbit response data in AGS Booster
Good agreements between AGS Booster data and Bmad model are reached, despite some faulty BPMs
Small discrepancies (within 1 mm) beyond error bars is being investigated to better calibrate model to real machine
Goal: produce accurate real-time predictions for operators and give tuning suggestions to improve beam quality

## Slide 24: Extraction bump fitting interface
NASA Space Radiation Laboratory (NSRL) takes beam from AGS Booster via slow extraction
Current extraction bump gives large residual orbit
Goal: tune bump setting by specifying desired beam position and angle at extraction septum

## Slide 25: Bunch Merging

## Slide 26
AGS bunch merging
Before transferring to AGS, beam bunch is split into 2 longitudinally to reduce the space charge effect reduce emittance improve polarization
Bunches are later merged in the AGS
Tuning requires expert knowledge, is time consuming, and tend to drift over time
Controls: RF voltages & phases
Goal: Obtain good merged bunch profile
  Emittance preservation
    No particle lost, Gaussian, no baby bunches
  Stable final bunch profile
    Merged in the center, not shifting left/right or bouncing up/down
Real mountain range data showing 2-to-1 bunch merge in AGS
Wall current monitor (WCM) generates voltage vs time signal. Each separated in time by N turns (N accelerator periods)
end of squeeze & start of merge
end of merge
start of squeeze

## Slide 27
Bunch merge simulation results
Target functions
Agent learned functions
Julia simulator of the bunch merge process
Soft Actor-Critic (SAC) agent to minimize emittance growth: 10,000 initial samples + 4,000 training steps
Able to learn target functions pretty well

## Slide 28
Machine test – Julia agent
Initial
1st step
3rd step
Original
2nd step
RF functions
Bunch traces
Last trace
RF cavities voltages are initially set to close to 0 during merge period to intentionally decrease merge quality
RL agent trained on the Julia simulator is applied to correct RF settings
RL agent manage to find good RF settings, produce result similar to established machine optimum

## Slide 29: Electronic Logbook Upgrade

## Slide 30: Electronic Logbook
Record information ranging from meeting notes, to do lists, and critical operations
Current search feature only provides exactly what a user enters, difficult to find related entries without the exact words
Goal: provide custom sets of entries based on users’ interactions with the system

## Slide 31: Elog search upgrade workflow
Elog Database
NLP Preprocessing
Doc2Vec Model
Classification
Similar Entries
This assumes we have ALL entries from ALL elogs (e.g., RHIC, Machine Learning, personal elogs etc.)
Removes any punctuation, stop words, and empty entries. Tokenize each entry & save this information.
Gensim Doc2Vec model trains 100 epochs. Returns the top few similar elog entries.
SKLearn MultinomialNB classifier predicts any entry’s tag.
Return similar entries in order by most similar.

## Slide 32: Similarity by word
Polarization
Background ~ 70%
Beta ~ 69%
Polarimeter ~ 64%
Bunch ~ 63%
Excitation ~ 63%
Coherence ~ 62%
Emittance ~ 60%
Blue
Yellow ~ 94%
RHIC ~ 87%
Ramp ~ 84%
Power ~ 84%
Run ~ 82%
Fill ~ 80%
Delay ~ 79%

## Slide 33: Summary
Machine learning methods have been developed and tested at multiple experiments and accelerators at the RHIC complex
Promising results indicate that ML algorithms can be powerful tools for various optimization problems, suitable for fast and complicated tuning in real time
Digital-twin development is underway to establish accurate models for different accelerators, with a focus on the injection compound, which will remain for the EIC
  Better understanding of beam behavior in the early stages of the acceleration chain
  Facilitate offline development of optimization routines
Important beam qualities such as emittance and polarization will benefit from incorporation of ML algorithms in the control system

## Slide 34: Publications
[1] Y. Gao, W. Lin et al., “Applying Bayesian Optimization to Achieve Optimum Cooling at the Low Energy RHIC Electron Cooling System”, Physical Review Accelerators and Beams 25, 014601 (2022).
[2] W. Lin et al., “Simulation Studies and Machine Learning Applications at the Coherent electron Cooling experiment at RHIC”, in Proc. IPAC'22, Bangkok, Thailand, Jun. 2022, pp. 2387-2390.
[3] Y. Gao et al., “Bayesian optimization calibration of ionization profile monitor at the AGS complex”, in Proc. IPAC'23, Venice, Italy, May 2023, pp. 4444-4447.
[4] W. Lin et al., “Machine learning applications for orbit and optics correction at the Alternating Gradient Synchrotron”, in Proc. IPAC'23, Venice, Italy, May 2023, pp. 4460-4463.
[5] W. Lin et al., “AGS Booster model calibration and digital-twin development”, in Proc. IPAC’24, Nashville, TN, May 2024, pp. 3449-3452.
[6] R. Roussel, W. Lin et al., “Bayesian Optimization Algorithms for Accelerator Physics”, arXiv:2312.05667 [physics.acc-ph]
[7] X. Gu et al., “Enhancing beam intensity in RHIC EBIS beamline via GPTune machine learning-driven optimization”, in Proc. IPAC'24, Nashville, TN, May 2024, pp. 118-120.
[8] J. Maldonado et al., “Towards unlocking insights from logbooks using AI”, in Proc. IPAC'24, Nashville, TN, May 2024, pp. 3579-3582.

## Slide 35: Thank you!