## Slide 1
Polarized Deuteron Sources
March 10, 2025 | FrANK Rathmann (for Ralf Gebel)
Polarized Ion Sources and Beams at EIC, Community Wide Meeting, Stony Brook, March 10-12, 2025

## Slide 2
Review of Polarized Ion Sources
Some Historical Sources and the State-of-the-Art (from literature)
Requirements for Precision Experiments (see also V. Hejny & J. Slim‘s talks)
Tools @ COSY
Conclusion
Outline

## Slide 3
Description of first polarized proton sources:
INTERNATIONAL SYMPOSIUM ON POLARIZATION PHENOMENA OF NUCLEONS, Basel, July 1960
Review of early work:
SOURCES OF POLARIZED IONS BY W. HAEBERLI ANNUAL REVIEW OF NUCLEAR SCIENCE, Vol. 17, 1967
Review of recent techniques and state-of-the-art sources:
Zelenski, A. (2023). Polarized Ion Sources. Polarized Beam Dynamics and Instrumentation in Particle Accelerators. Springer, Cham. https://doi.org/10.1007/978-3-031-16715-7_10 https://rdcu.be/ecH5M
Sources of Polarized Ions

## Slide 4
Three-step process:
  Spin Filtering or Optical pumping
  Polarization Transfer
  Ionization
Examples:
  (First Sources)
  CIPIOS / INR / HIAF
  NICA
  COSY
Polarization Techniques

## Slide 5
Basics: Select your Spin State…
Bc = 117 G
Bc = 507 G
Deuterium
Hydrogen

## Slide 6
Ionization by electron bombardment (NIM 25 (1963) 67-76)
Improvement by strong field ionizers (e.g. Glavish NIM 65 (1968) 1-7) with confinement of electrons in a solenoid: from 0.2 µA to ~ 0.5 µA p P = 90 %
First polarized protons / deuteron sources

## Slide 7
Negative polarized deuterons
H0 beam 0.4x1016 /s
H+ beam 0.15 mA = 1012 /s
H- beam 0.15 nA =108 /s
P = 0.47 (weak field)
Ionizer: 0.2A electrons, 250 eV
Ionizer efficiency 0.25x10-4
First source of negative polarized D (1964)
Gruebler, Schwandt, Yule, Haeberli
NIM 41 (1965) 245-254)

## Slide 8
From µA to mA intensities (Bonn 1982 - 1988)
Solenoid
(<4 Tesla)
1st 6-Pole
2nd 6-Pole
IF
WF
1.8 m
Penning
Ionizer
Dissociator
6-Poles &
Transitions
System with 8 electrostatic electrodes,
magnetic and electrostatic mirror.
Strongly coupled system with hysteresis
Large potential depression
Noisy
System with compressor (2nd) 6-pole magnet
and tapered (1st) 6-pole magnet.
Transitions suffer from the stray-field of the solenoid
Beam handling matched to cooled nozzle
Polarization suboptimal
Nozzle cooled to 77K

## Slide 9: Precision of beam control: Penning vs. ECR
Eversheim et al.
NIM A 371 (1996) 345-350
Lesson learned: Source quality is mandatory.

## Slide 10: From µA to mA intensities: Quality is mandatory
Penning ionizer
ECR Ionizer

## Slide 11
A method based on a proposal from 1968 (NIM 63, page 335):
The process H0  D- → H- + D0  is a resonant charge transfer process. The cross section increases with decreasing relative velocity and reaches:
At INR Moscow 5 mA with 95% polarization
Exceeding (pulsed) 5 mA intensity
s = 22x10-16cm2 at 2 keV -> 100x10-16cm2 at 10eV

## Slide 12: INR-RAS: Unique plasma injector of deuterium plasma enriched by D- ions (A. Belov et al.)

## Slide 13
CIPIOS: THE source for COSY‘s scLinac (2002)
V.P. Derenchuk et al., Workshop on Polarized Sources and Targets, Erlangen 1999

## Slide 14
NICA polarized Deuteron ion source
A S Belov et al 2017 J. Phys.: Conf. Ser. 938 012017 DOI 10.1088/1742-6596/938/1/012017

## Slide 15
IMP polarized ion source for HIAF (EicC)

## Slide 16
NIM 62 (1968) 355-357
Electron transfer from atoms or ions
First test (Wisconsin): 1 mA H- - high polarization (90%).
COSY/Jülich: up to 50 mA H- (*1993/ D-2003– 2023)
W. Haeberli (1968): transfer an electron from Cs to H0
H0+Cs0 (30keV) -> H-+ Cs+ (s= 4x10-16 cm2)
Cs
Cs+ (30 keV)
Cs
H0
B

## Slide 17
COSY/Jülich: polarized H-/D- source

## Slide 18
Source Experience
  1986 - 1989 Atomic beam source with Penning ionizer (Bonn)
  1989 - 1995 Atomic beam source with ECR ionizer (PSI, ETH, Bonn)
  1993 - 2023 Atomic beam source with colliding beams ionizer (COSY/Jülich)
  1995 - OPPIS (@TRIUMF); SABPIS (Cologne), Lambshift (FZJ), LASER-based …
  2001 - 2003 CIPIOS Atomic beam source with plasma ionizer (IUCF)
  (+ unpolarized …)
Two favorites:
  BNL’s OPPIS (p) @ BNL and
  IUCF’s CIPIOS (p & d), selected (for COSY’s scLinac), NICA & HIAF
Review – Hands-on experience

## Slide 19: Spin Manipulation Tools @ COSY
Polarimeter (JEPO, EDDA, LSP, LEP, BRP)
Wienfilter (DC classical ExB)
Solenoids (nc)
Siberian snake (sc, “fast” ramping)
AC dipoles and solenoids
Fast kickers/correctors
Fast Q-Jump quadrupoles
KO exciter and spill optimization by feedback
Orbit control with precision and feedback
Dynamic Tune and Chromaticity Control
AI applications: intensity, orbit,…

## Slide 20
Fast set-point and process value monitoring (archive!)
Appropriate accelerator model and simulation
Visualization (fast and “good enough”)
Beam control
  Intensity and availability
  Orbit control
  Momentum distribution (cooling, bunching, shaping, extraction, …)
  Polarization handling (preservation, coherence, flip, spin tune lock, …)
  Application of AI
Sophisticated DAQ and Beam control

## Slide 21: Application of machine learning - 2023
COSY (2023): Awal: AI for intensity and beam localization

## Slide 22
Select your state-of-the-art source model: PI w/o storage cell)
Combine it with excellent diagnostics and control/feedback systems
Apply AI methods (Simulation, digital twins, …)
Continuous improvement is mandatory
Conclusion