## Slide 1: Extraction and transport from AGS for fixed target experiments
10 July 2025
Advancing Nuclear Physics:
New Horizons with Fixed-Target Proton-Nucleus Experiments at Intermediate Energies
Kevin Brown
Brookhaven National Lab

## Slide 2: Outline
Overview of AGS Extraction systems
Slow Extracted Beams
Fast Extracted Beams
Applications and Requirements
Electronics testing for Space Radiation Environment
Detector Test beams
Proton radiography
Nuclear physics
Beam transport options
Slow extraction to Bldg. 912
Beam Quality and methods to improve duty factor

## Slide 3: Overview of AGS Extraction systems

## Slide 4
Old Fixed Target Area
An old image but shows 3 things.
Fixed target Area (912)
  Slow extracted beams
  Single bunch fast beam
  Micro & mini-bunched SX
G-2 with fast single bunch
  12 bunches, 33msec apart
AtR, with fast single bunch

## Slide 5
We used to handle a large variety of experiments.
After 2002
all HEP experiments ended
NP experiments ended with RHIC startup
NASA moved to new facility off the AGS Booster
G-2 finished
Radiography ran 1 year

## Slide 6
Ways to extract beam from the AGS
1. Fast beams (single bunches)
  To Uline via G10 kick into H10 Septum
  OR
  To 912 (A,B,C, or D) via G10 kick into
  F5 and F10 Septa (requires correct horizontal tune)
2. Slow extracted beams (1 – 2 seconds long)
To 912 via F5 and F10 septa
3. Slow extracted modes
Bunched beam slow extraction
Micro-bunched beam slow extraction
We do not have the ability to extract full turn. This would require a new kicker magnet.
Booster
AGS
H10
Septum
Single bunch
Kicker, G10
F10
Septum
F5
Septum
F7 Bump
U line
Bldg 912
D
A
B
C
Slow extracted high intensity protons split into 4 beams (2001)
Slow extracted high intensity protons 2 second spill (2001)
As Vincent already showed

## Slide 7: Overview of AGS Slow Extraction
Thin Septum
0.76 mm, 1.5 kG
Thick Septum
13.5 mm, 9.5 kG

## Slide 8: AGS Performance History
PROTON BEAM FY94 FY95 FY96 FY97 FY98/99 FY2000
SEB FEB (g-2) SEB FEB (g-2) FEB (g-2)
Beam Energy 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV 24 GeV
Peak Beam Intensity 40 x 1012 ppp 63 x 1012 ppp 62 x 1012 ppp 62 x 1012 ppp 46 x 1012 ppp 72 x 1012 ppp 58 x 1012 ppp 61 x 1012 ppp
Total protons accelerated 0.3 x 1020 1.1 x 1020 0.9 x 1020 0.4 x 1020 0.1 x 1020 0.9 x 1020 0.4x 1020 0.5x 1020
Spill Length/Cycle Time 1.0 sec/3.8 sec 1.6 sec/3.6 sec 1.6 sec/3.6 sec 1.6 sec/3.6 sec 2.8 sec/5.1 sec
-> Duty Cycle 26% 44% 44% 44% 55%
Spill Structure Modulation
(peak-average) /average 50% 20% 20% 20% 20%
Average Availability
/Best Week ~83% 82%/ 93% 76% / 92% 71% / 79% 58 % / 67 % 71% / 88% 55 % / 83 % 74 % / 87 %
HEAVY ION BEAM Au Au Au Au Fe (NASA) Au Fe (NASA)
Beam Energy /nucleon 11 GeV 11 GeV 11 / 4 / 2 GeV 11 / 8 / 6 GeV 1.0 / 0.6 GeV 11 GeV 1.0 / 0.6 GeV
Peak Beam Intensity 2 x 108 Au/p 2 x 108 Au/p 4 x 108 Au/p 17 x 108 Au/p 20 x 108 Fe/p 9 x 108 Au/bunch 36 x 108 Fe/p
Spill Length/Cycle Time 1.0 sec/3.8 sec 1.0 sec/3.8 sec 1.4 sec/3.6 sec 1.5 sec/4.0 sec 1.2 sec/3.0 sec
-> Duty Cycle 26% 26% 39% 38% 40 %
Spill Structure Modulation
(peak-average) /average 50% 20% <20% <20% <20%
Average Availability ~85% 90% 80% 82 % 96 % 81 % 90 %

## Slide 9: Applications and Requirements

## Slide 10: Various Users are looking for beam
Electronics testing to replicate space radiation effects
  NASA, MDA, SpaceX, Blue Origin, ESA, etc.
  Need low energies = 100 MeV/n to 2 GeV/n
  Need many different ions (protons to Bismuth)
  Large uniform beams + smooth, long spills
Detector test beams (big demand, no supply for next few years)
Imaging dense materials (radiography – HE protons, no supply)
NP experiments

## Slide 11: Historically, NP requirements
Slow extracted beams mostly with Au
  Energy scans
  Specialized targets
  Well focused (point sources) on target
All standard experimental support services
  Riggers, electricians, etc.
  Engineering support for detector installation
  Physics support to liaison with accelerator department
  Communications (network for data links, etc.)
  Counting houses with A/C

## Slide 12: Beam transport options

## Slide 13: Status
Slow extraction from AGS has been disabled, to re-enable we need
New thin and thick septa magnets and power supplies
F7 bump reinstalled with new cables and new PS
4 sextupole magnets reinstalled and new PS
New active filter (to reduce spill ripple)
New vacuum pipe from F10 to F12, for extraction channel
Refurbished magnets in 912
Refurbished and possibly new PSs for magnets
New vacuum systems
New instrumentation

## Slide 14
Building 912 today
Most of the old switchyard is still in place.
But,
Not operated in 25 years.
All formed experiments and detectors have been removed.
Some magnets have been removed, to repurpose and use for other applications.
Electrical infrastructure does not meet code – needs upgrading before running.
EEBA no longer available!

## Slide 15: Features of old Switchyard
Beams were split to four primary targets
    Requires 3 electrostatic splitters and 3 movable Lambertson magnets
    Features complicated vertical trajectories for each beam line

## Slide 16: Options
We could do split beams again, but we would simplify the design.
How many beamlines are needed?
We would look into horizontally splitting, rather than vertical
Handling momentum dispersion will be an issue. Would want to design achromatic tune and split where D=D’=0.
We could eliminate splitters and use a switching magnet
If each beamline has a different purpose this is the best option
Can NP experiments share a single target?
Electrostatic splitter
Thin Lambertson
Thick Lambertson

## Slide 17
For Example: 3 different Users
Test Beam or NP Experiment
US1 might be electronics testers
Best use of Dline is for low energies
Designed to give large uniform beams created using octupole magnets
US2 may be anything
Designed to give large uniform beams but by rastering a small beam.
Could deliver small beams on a target.
Switching magnet

## Slide 18: Beam Quality and methods to improve duty factor

## Slide 19: Main beam quality issues to consider
Spill quality
  Historically it was usually around 30-40% modulated
  Modulation comes from tune ripple in the AGS (ripple on power supplies modulate the tune during extraction)
  Active filter (on AGS Main magnet PS) helps
  Additionally, could add high frequency quadrupole and modulate to remove the ripple structure (have such system Booster, R&D project)
Beam size and shape
  We can make small Gaussian shaped beams (~ a few mm diameter)
  We can make various size uniform beams. But using octupoles to do this gets harder with high energy beams. Rastering is a better approach.
Beam Motion on target
  Historically a challenge in the switchyard. No dispersion control.
  Two ways to fix it: ramp dipoles with spill or design achromatic tune.

## Slide 20
Samples of Spills
2.2 Seconds
AGS 2001 high intensity protons
JPARC has some unique problems, due to operation with zero chromaticity.
CERN SPS
CNAO, MedAustron, Italy
Air core quad feed forward

## Slide 21: Beam distribution
Typical beam profile, captured on the Digital Beam Imager (DBI), and analyzed using ImageJ. This is an image formed from one full spill.
The projections show the beam spatial distribution to be within a few % of the mean in the area between the outer “ears”.
20 cm
Uniform Beams at NSRL (NASA beamline of the AGS Booster)

## Slide 22
Images from Heavy Ion running in 1997, 11.68 GeV/n Au
Species | Year/Run | Frequency {MHz} | Harmonic | Momentum {GeV/c/n}
Au | FY97 10.6GeV | 4.443350 +/- 20Hz | 12 | 11.71
Au | FY97 8GeV | 4.43296 +/- 50Hz | 12 | 8.859
Au | FY97 6GeV | 4.41680 +/- 50Hz | 12 | 6.841
Fe | FY97 1GeV | 3.9585 +/- 100Hz | 12 | 1.80
Fe | FY97 0.6GeV | 3.539215 +/- 100Hz | 12 | 1.215
Au | FY96 10.6GeV | 2.96224 +/- 20Hz | 8 | 11.69
Au | FY96 4GeV | 2.918984 +/- 50Hz | 8 | 4.883
Au | FY96 2GeV | 2.8180 +/- 50Hz | 8 | 2.783

## Slide 23: Questions?