## Slide 1: Accelerator Technology for the EIC
June 3, 2026
Christoph Montag, BNL

## Slide 2: From RHIC to EIC
RHIC:
Two superconducting ion storage rings
3.8 km circumference
6 interaction regions, 2 detectors
Beam energy up to 255 GeV for protons, or 100 GeV/n heavy ions
110 bunches per beam
Ion species from protons to uranium
60% proton polarization – world’s only polarized proton collider
Exceeded design luminosity by factor 44
In operation since 2001

## Slide 3: EIC Design Concept
EIC is based on the RHIC complex: Hadron Storage Ring (HSR), injectors, ion sources, infrastructure; needs only relatively few modifications and upgrades
Todays RHIC beam parameters are close to what is required for EIC (except number of bunches, 3 times higher beam current, and vertical emittance)
Add a 5 to18 GeV electron storage ring & its injector complex to the RHIC facility  Ecm = 29-141 GeV
Design and built a suitable interaction region
EIC design aims to meet the goals formulated in the EIC WHITE PAPER, in particular the high luminosity of L = 1034cm-2s-1 and high polarization

## Slide 4: EIC Design and Performance Parameters
RHIC
Hadron Ring
Choice of EIC beam performance parameters informed by parameters achieved at other facilities: RHIC, HERA, KEK-B
Parameters backed up by comprehensive & systematic simulation studies: Beam-beam, dynamic aperture, instabilities & collective effects, sensitivities to imperfections
Some of the EIC parameters and assumptions tested experimentally in RHIC: generation of and collisions with flat hadron beams, or extreme off-center/off energy operations to operate at different energies with the same revolution frequency
Feasibility of EIC Design Parameters: Generation of & collisions with flat hadron beam demonstrated in RHIC, emittance ratio

## Slide 5: Facility layout
“Yellow” RHIC ring as EIC Hadron Storage Ring
RHIC hadron injector complex, with new, room temperature injection line to IR4
5 – 18 GeV Electron Storage Ring (ESR) in the same tunnel
750 MeV to 18 GeV Rapid Cycling Synchrotron (RCS) as electron injector in a separate, 1.4 km circumference tunnel
Interaction Region (IR) with ePIC detector in IR6

## Slide 6: Luminosity versus Center-of-Mass Energy

## Slide 7: Parameters for Highest Luminosity
Hadron beam parameters similar to present RHIC, but smaller vertical emittance and many more bunches
2 hour IBS growth time requires strong hadron cooling
Electron beam parameters resemble a B-Factory (PEP-II, KEKB)

## Slide 8: The EIC Hadron Storage Ring HSR
EIC HSR to be composed of existing arcs of the Yellow RHIC ring (remove unused magnets)
Insert sleeves coated with copper and amorphous carbon into superconducting magnet beam pipes to improve conductivity and reduce secondary electron yield (-> electron cloud)
Add new RF cavities
Add hadron cooling to create ‘flat’ bunches
Add crab cavities, new IR SC magnets
Add a collimation system
CD-3A: Actively Cooled Beam
Screen Material procurement
Tripled beam current, shorter bunch length, shorter bunch distance, ‘flat’ beams with small vertical emittance

## Slide 9: Beam Energy and Average Orbit Radius in the HSR
Since the electron revolution frequency is fixed, the hadron orbit must be adjusted with energy to keep the collisions in sync.
Demonstrated at RHIC
70 mm beam pipe
20 mm
275 GeV
100 GeV
store
130 GeV

## Slide 10: The 41-GeV ‘bypass’
Sector 1 without and with the 41-GeV bypass line

## Slide 11: Intra-beam Scattering (IBS)
Individual particles in the beam are focused by the magnets
As a result, individual particles are constantly moving within the bunch
As particles pass each other, they scatter off each other
This multiple scattering results in emittance growth – the denser the bunch, the faster the growth
If not counteracted, emittance growth results in luminosity degradation
Electron beams have synchrotron radiation damping to counteract (IBS), but hadron beams need cooling

## Slide 12: Hadron Beam Cooling
Conventional electron cooling
  Energy exchange between stored hadrons and an intense, “cold” (= low emittance) electron beam
  Transverse cooling times scale as - very challenging (but not impossible) above a few GeV

## Slide 13: Hadron Beam Cooling
Stochastic cooling
  Measure the 3D offsets of small subsets of the particles in a bunch, and correct them a short distance downstream
  Synchrotron motion in the rest of the ring leads to mixing of particles, such that each time these subsets consist of different particles with non-zero net offsets
  Cooling time proportional to (system bandwidth)/(number of particles per bunch). Few GHz bandwidth leads to ~30 minutes cooling time for particles. Suitable for heavy ions in EIC, but not for protons due to factor 100 higher bunch population

## Slide 14: Hadron Beam Cooling
Coherent electron cooling
  Essentially, an ultra-high bandwidth stochastic cooling system
  Instead of conventional pick-up, amplifier and kicker, and electron beam serves as pick-up and kicker
  Hadron beam distribution is imprinted on electron beam
  This imprinted signal is amplified, for example in a free-electron laser (FEL)
  Electron beam is then merged again with the hadron beam (with the correct phase) to serve as a kicker and “correct” the hadron beam distribution
  Bandwidth: tens of THz

## Slide 15: EIC Electron Storage Ring
Electron Storage Ring (ESR) consists of six FODO-cell arcs, and six straight sections (IRs)
Straight sections are used for:
  Detectors (IR6 and IR8)
  RF cavities (IR10)
  Injection and cross-over with HSR (IR12)
  Instrumentation (IR2)
  Cross-over with HSR (IR4)
Replace figure

## Slide 16: Emittance Control in the ESR
EIC needs nearly constant (20 to 24 nm) emittance from 5 to 18 GeV for optimum luminosity, but equilibrium emittance in an electron storage ring depends on beam energy:
Betatron phase advance μ per FODO cell is the “knob” to adjust the emittance
60 degrees at 10 GeV and 90 degrees at 18 GeV yield 20 nm at 10 GeV, 24 nm at 18 GeV
“Super-bends” (reverse bends) for emittance generation below 10 GeV – pole width accommodates the ~20 mm orbit variation
Rotating coil field measurements to be taken along different paths to reflect these orbit changes
Feed-down due to off-center orbits taken into account in dynamic aperture tracking

## Slide 17: EIC Electron Polarization
Physics program requires bunches with spin “up” and spin “down” (in the arcs) to be stored simultaneously
Sokolov-Ternov self-polarization would produce only polarization anti-parallel to the main dipole field
Only way to achieve required spin patterns is by injecting bunches with desired spin orientation at full collision energy
Sokolov-Ternov will over time re-orient all spins to be anti-parallel to main dipole field
Spin diffusion reduces equilibrium polarization
Need frequent bunch replacement to overcome Sokolov-Ternov and spin diffusion

## Slide 18: Electron polarization in the ESR
Frequent injection of bunches with high initial polarization of 85%
Initial polarization decays towards P∞
At 18 GeV, every bunch is replaced (on average) after 2.2 min with RCS cycling rate of 1Hz
B P
Refilled every 1.2 minutes
B P
Refilled every 3.2 minutes
Pav=80%
Pav=80%
Re-injections
P∞= 30%
(conservative)
Re-injection

## Slide 19: Electron Injector System
750 MeV linac @ 3 GHz Copper RF
fRF = 591 MHz
RCS
RF
28 x 1 nC single bunch injection
ESR
RF
In RHIC tunnel
Swap out
1.4 km circ.
0.75 to 18 GeV at 1 Hz
BAR
28 nC/bunch
accumulator
ring
at 30 Hz
Rapid Cycling Synchrotron in new, separate 1.4 km tunnel
Spin transparent due to high periodicity, high vertical tune
Frees up valuable space in collider tunnel

## Slide 20: Luminosity and Focusing
Strong focusing by =5 cm
Luminosity ~ 1/(spot size)
A smaller spot size at the IP means more luminosity
At the IP, (beam size)X(beam divergence)= const. in each plane (emittance)
For a given beam (= fixed emittance), a smaller IP beam size means larger divergence
A larger beam divergence leads to a larger beam size at the nearest focusing magnets – (size at magnet)=(divergence)X(distance)
Magnets need to have larger aperture while gradient (= focusing strength) remains the same – peak field at magnet poles is technically limited
Focusing elements for both beams need to be as close as possible to the IP

## Slide 21: Crossing angle collisions
Beam energies of electrons and hadrons are vastly different in EIC
Focusing elements for electrons would have only little effect on hadrons, while hadron magnets would overfocus electrons
Beams need to be separated into their respective focusing systems as close as possible to the IP
A separator dipole would have to deflect the (“weaker”) electrons and would therefore generate a wide synchrotron radiation fan that would need to pass through the detector – requires large beam pipe diameter (HERA-II)
Best solution: Crossing angle collisions!

## Slide 22: Crossing Angle and Luminosity
Long (~+/-6 cm), skinny (100 um) bunches colliding at an angle have very little overlap
With 25 mrad crossing angle, each particle can only interact with a +/-4 mm thick slice of the +/-6 cm long oncoming bunch
In head-on collisions, every beam particle in one beam can potentially interact with every particle in the other beam

## Slide 23: Crab Crossing to the Rescue
Head-on collision geometry is restored by rotating the bunches before colliding (“crab crossing”)
Bunch rotation (“crabbing”) is accomplished by transversely deflecting RF resonators (“crab cavities”)
Actual collision point moves laterally during bunch interaction

## Slide 24: Nobody’s perfect
Bunch rotation (crabbing) is not linear due to finite wavelength of RF resonators (crab cavities)
Long hadron bunches are “S”-shaped during collision
Distorted shape results in transverse offset between electron bunch and head and tail of proton bunch – reduced luminosity and severe beam dynamics effects
Longer bunches, skinnier bunches, or increased crossing angle all make this worse
Higher harmonic crab cavities can “straighten out” the kick and therefore the bunch, but at a cost – space and money
EIC already plans on 197 MHz crab cavities, plus 394 MHz harmonics
197 MHz as low as technically feasible (niobium sheets for cavity production, cavity size in tunnel)

## Slide 25: 197 MHz Crab Cavity - Design & Prototyping
197 MHz Cavity String
Cryomodule
Each cryomodule has two 197 MHz crab cavities
HOM Dampers are installed on superconducting ‘dogbone’ waveguides, shown between the cavities
The size of the cavities and cryomodule create challenges in assembly and integration into the tunnel
The cavity string went through a Preliminary Design Review in 2024
Design Verification Component (DVC)
A prototype (DVC) cavity is being fabricated in-house at JLab
The cavity will be tested at 2K in the JLab VTA
EBW of niobium parts for the cavity is currently underway

## Slide 26
EIC Near-detector IR Layout
IR based on 25 mrad total crossing angle, compensated by crab crossing
No electron dipoles within ~30 meters upstream of detector
Large aperture superconducting magnets to accommodate forward scattered particles and synchrotron radiation photons
Note: Colored “boxes” indicate magnet apertures

## Slide 27: Forward Acceptance
Physics requires detection of charged particles with transverse momentum 200 MeV/c < < 1.3 GeV/c
These particles are detected by “Roman Pots” along the forward hadron beamline, at about 10σ from the central orbit
For scattered particles to be detectable in Roman pots at 10σ, their scattering angle at the IP must be greater than 10. This constrains the beam divergence and therefore the lowest hadron
For = 1.3 GeV/c, and for the +/- 4 mrad neutron cone, hadron magnet apertures in the forward direction must be large enough to allow these particles to pass through

## Slide 28: Forward Spectrometer – the B0pF Magnet
Spectrometer “dipole” B0pF adjacent to main detector on “forward” side
Large aperture combined function magnet, with detector elements inside
Electron quadrupole Q0eF inside B0pF aperture

## Slide 29: Forward Spectrometer – the B0pF Magnet
B0pF is actually a combined function magnet aligned with electron orbit, thus minimizing dipole field on electron orbit
Quadrupole component of B0pF matches required quadrupole field for 10 GeV electrons
Q0eF quadrupole to adjust gradient on electrons at 5 and at 18 GeV
External field of Q0eF quadrupole impacts multipole harmonics on hadron beam
Space for detector elements

## Slide 30: Synchrotron Radiation
Synchrotron radiation is generated in upstream (“forward”) magnets
Dipoles are placed far away and split into two segments (weak and strong bend) to further reduce synchrotron radiation power
To avoid high photon background rates, radiation fan has to be passed through the detector beam pipe as well as through downstream (“rear”) magnets to a faraway absorber
Rear electron magnet aperture requirements are determined by synchrotron radiation photon fan, not by the much smaller electron beam itself
See:
Collimation and MPS, A. Natochii

## Slide 31: Luminosity Measurement
Luminosity measurement is based on Bethe-Heitler (bremsstrahlung) photons generated at the IP
Bethe-Heitler photons travel within the synchrotron radiation fan
Photon energy is much higher than synchrotron radiation – separation by exit window
Exit window converts high energy photons into e+e- pairs that are detected in a tagger

## Slide 32: Spin Rotators
Hadron spin rotators are based on helical dipoles – same as RHIC
Electron spin rotators are based on superconducting solenoids – one set for 5 GeV (lowest energy) and one set for 18 GeV (highest)
Each solenoid is split into two halves with normal-conducting quads in-between for local decoupling (no skew quads)

## Slide 33: Summary
The EIC is a very complex, challenging machine:
  High luminosity
  Polarized beams
  Crab crossing
  Beam cooling
  Large energy range
  Flat hadron beams
  …
EIC meets requirements laid out in the CD-0 Mission-need Statement
A couple of crucial design changes were made, notably on the RCS
Design is well underway, preparing for CD-2/3
CD-4 envisioned in 2034

## Slide 34: Backup Slides

## Slide 35: B1pF – Prototype Collared Magnet
Magnet Cross-section | Value
Number of Conductors per quadrant | 63
Margin on the loadline | 42.4 %
Reference Radius | 75 mm
Nominal Current | 11900 A
Central Field (Rref=75 mm) | 4.128 T
Diff. Inductance | 26.7 mH
Max. peak field (on block 6) | 5.1 T
Stored energy | 1.89 MJ
Parameter | Requirement
Nominal Integrated Field | 10.344 T.m
Total slot length | 3.0 m
Aperture radius | 150 mm
Reference Radius | 75 mm
Operating Temperature | 1.9 K
Harmonics | All <1 unit
Field in electron beam tube | As low as possible
Design Goals
Optimized coil specs

## Slide 36: SC Magnet Updates: Current status of B1pF prototype
Shown below are pictures of the B1pF Cable magnet prototyping effort underway at SMD.
The image on the right is a complete half length coil just prior to being moved into the curing press.
Shown above is a test wind that was performed in July/Aug 2024

## Slide 37: Tapered CCT Magnets Hadron Forward Side
Idea: replace hadron forward collared magnets
Instead of 5 collared magnets: 3 tapered CCT magnets
  Q1ABpF
  Q2pF
  B1/B1ApF
Technically and financially attractive
  Eliminates/reduces beam going through quads at an angle/off center
  Frontloading of gradient
  Reduces crosstalk
IP
Electrons
Hadrons

## Slide 38: Q1ABpF – New Magnet Concept
275 GeV
41 GeV
100 GeV
275 GeV +1.3 GeV px
275 GeV -1.3 GeV px
New magnet – Q1ABpF
Advantages: No end plates, making use of additional space between magnets
Smaller aperture at IP side, can tune field/gradient for crosstalk
Recombining Q1ApF and Q1BpF
(similar for other magnets)
 | L (m) | G (T/m)
Q1ApF | 1.46 | -77.903
Q1BpF | 1.61 | -63.028

## Slide 39: Q1ABpF: Implementation
Q1ABpF
Q1eF
R=50mm
CCT
  Allows to cancel unwanted harmonics
  Modulation of gradient
Frontloading of gradient
Helps crosstalk / field quality
  Better utilization of space
  Can tailor maximum gradient
Challenges
  Need to prove that this works mechanically (no collar)
Requirements
  Integrated gradient 215T
  Very good field quality
Design needs to be updated
  Q1ABpF prototype experience
100 → 50 T/m
J1
J2
JΣ
3.5m
Radius=59mm..93mm

## Slide 40: Q1ABpF – Short Prototype
Short Q1ABpF: driven by schedule considerations
Design features
  ~0.84m from IP end
    High gradient/field
  Can be done with cable/strand at hand
  Reduction of layers from 16 to 12
    Accomplished by adjusting spacing/tilt angle
    Reduces winding time
    Crosstalk
Goals
  Demonstrate feasibility of Q1ABpF (full length version)
  Feasibility of large aperture, high gradient direct wind quadrupole
0.8m
87T/m
Length=0.8m
L=86.7mH
I=1360A
E=80kJ

## Slide 41: SC Magnet Updates : Current status of Q1ABpF
Tapered dipole
All 12 layers successfully completed in February
First layer

## Slide 42: Magnet Shimming – Tunability
Using two shims in dedicated cutouts, b3 can be tuned by a range of (+9.8 -8.6) units
B5 can be tuned to (+0.5-1.0) units
Additional tunability can be achieved by adding further shims on the coil wedges
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 7 | 9 | 11 | 13
b2 | 0.020785 | 0.020582 | 0.020987 | 0.0212 | 0.021132 | 0.021611 | 0.022341 | 0.022924 | 0.023405 | 0.024385
b3 | 8.5135 | 6.9454 | 5.457 | 4.0401 | 2.6911 | 1.4044 | -1.9468 | -4.401 | -6.6034 | -8.5832
b5 | 0.31721 | 0.24456 | 0.17214 | 0.10168 | 0.033004 | -0.033416 | -0.20076 | -0.33662 | -0.46277 | -0.5774
Harmonics as a function of Shim 1 depth
Chart: 
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Filled shim | 0.23381 | 6.5199 | 0.03866 | -0.21157 | 0.0037396 | -0.021883 | 0.0006302 | -0.36965 | 0.00010758 | 0.33339 | 3.7023e-05 | 0.10173 | -3.8897e-05 | 0.041893
Unfilled shim | 0.23687 | -6.8461 | 0.037725 | -0.13644 | 0.0035348 | 0.14523 | 0.00031007 | -0.35521 | -6.7677e-05 | 0.33554 | -0.00010065 | 0.10233 | -4.0493e-05 | 0.042139
Filled shim1 | 0.25388 | 9.8029 | 0.03791 | 0.20205 | 0.0033835 | -0.073207 | 0.00013128 | -0.37505 | -0.00024868 | 0.33426 | -0.0001082 | 0.10183 | 9.543e-05 | 0.041972
Filled shim2 | 0.21618 | -8.6343 | 0.039235 | -0.54023 | 0.0040206 | 0.18437 | 0.00032331 | -0.35017 | -0.00015372 | 0.33461 | -0.00021749 | 0.10216 | -9.6547e-05 | 0.042036