## Slide 1: Tracking Detectors
TK Hemmick

## Slide 2: Pop Quiz Hot Shot
You already learned about calorimetry from Ross Corliss.
Let’s test your knowledge and use it to justify the need for tracking detectors.
Question 0: What movie is that?

## Slide 3: Particle Interactions with Matter
Four fundamental forces: Gravity, Weak, E&M, strong
Participants
  Pion Strong, E&M
  Proton Strong, E&M
  Muon E&M
  Electron E&M
    Bremsstrahlung sets in for the electron.
    Allows short detector
    Allows high precision
Infinite Block of Material
pion
proton
muon
electron
Medium Range
Long Range
Short Range
Question 1:
How do you compare the range over which these different particles lose their energy in matter?

## Slide 4: Different Styles One Goal
All calorimeters shower.
Collection Varies
Question 2:
How does the energy resolution vary with the energy?
Shower Particles  Light  Sensor
UV  Visible  Sensor
Cheap Redirection
Light w/in Fibers  Sensor
Electron  Accordian  Back

## Slide 5: Calorimeter Energy Resolution
Fundamentally the calorimeter “counts” something (charge particles, ionization, photons, …) that is proportional to the energy deposit.
  Statistical Term:
  Scale/Calibration Term:
  Noise Term:
  Full Resolution
C1 = 3.5%
C2 = 13.3%
Often
negligible
Question 3:
For which energies to you abandon Calorimetry and Search for a different solution?

## Slide 6: Calorimeters vs Spectrometers
Calorimeters
  Measures energy
  Best energy resolution at highest momentum/energy
  DESTRUCTIVE to the particle (cannot measure again)
Magnetic spectrometers
  Measures momentum
  Best momentum resolution at lower momentum
    Position Resolution:
    Multiple Scattering:
    Total:
  Non-destructive to the particle:
    Gas remains the lowest radiation length (X0) material…study that first!
    Good news: little energy loss to the gas; Bad news: tiny signals!
a
Question 4:
Which should particles encounter first trackers or calorimeters & why?

## Slide 7: Electron Motion in a Gas
Low electric fields
  Collisions of electrons with gas molecules provide an effect backward “Force” on the electron proportional to velocity:
  Terminal velocity when
    Ions are simple (“b” is effectively constant and
    Electrons are more complicated as “b” depends upon v
High Electric Fields
  Electrons gain enough energy in a mean free path that they are capable of ionizing the gas.
  Exponential growth in electron current:
  Growth controlled by the Townsend Coefficient, a.
Virtually all gas detectors use a low electric field to drift electrons into an avalanche region for detection.

## Slide 8: Geiger-Muller  Charpak (Nobel 1993)
With a pure noble gas, photons from the avalanche create ionization in the outer region.
The avalanche “runs away”
  Good news: BIG signal
  Bad news:
    Dead time while wire recharges
    Insensitive to energy deposited
Complex molecules have the ability to absorb energy as vibrations and rotations.
Adding this “quench” to the gas breaks the feedback loop.
“Proportional Counter’

## Slide 9: Gas Chamber Evolution
Positive Cloud Around Wire
Segmented Pad Plane
MWPC
Drift Chamber
Pad Plane
Time Projection Chamber

## Slide 10: Beyond the Wire Chamber: MPGD
To get a strong avalanche, wires must be thin.
Thin wires are fragile.
Micro-Pattern Gas Detectors:
  Seek to use modern techniques to manufacture mechanically robust electrodes.
  Many competing concepts available today.
Micro Strip Gas Chamber (MSGC)
Anton Oed, 1988
The first MPGD.
Lithographic “wires”.
Launched a new field.

## Slide 11: Most common MPGDs in use Today
microMEGAS
Gas Electron Multipliers GEMs
Fabio Sauli
Ioannis Giomataris

## Slide 12: Cutting Edge Alternatives
Burgeoning field.
Developments favoring PID will be in tomorrow’s lecture.
Thick GEM
Macro Pattern Gas Detector
Drilled Holes
mRWELL
RPWELL

## Slide 13: Precision of Gas Measurements
Many factors can affect resolution, but two terms affect all detectors.
  Readout Intrinsic Resolution
    Constant…segmentation, noise, etc…
  Diffusion
    Diffusion is a transverse kick due to electron-molecule collisions
    Diffusion follows the mathematics of a random walk.
    A single electron “misses” it’s target by
    The error on the mean of N electrons received is
  Other effects are either sensitive to the number of electrons in a signal or not. The typical formula becomes:
  Notice that transverse diffusion falls STEEPLY with magnetic field.
has units of
Modern Gas Detectors achieve resolutions of

## Slide 14: sPHENIX TPC Example

## Slide 15: From Gas to Solid Detectors
Downside:
  Solids are denser and give more multiple scattering and Bremsstrahlung.
Upside(s):
  Energy deposit is ~103-4 times greater  No avalanche.
  PCB technology (~100 mm)  Chip Technology (~0.1 mm for MAPS)
Ionization Electrons Flow Briefly  signal!
When a diode is reverse biased, the current flow stops.
Silicon Detector c. 1970
Still a staple today:
Simple measurement.
High Electron Statistics
Good energy resolution

## Slide 16: Segmentation starts the Revolution!
Bond by “rubbing”
Tiny Connections
1970’s Silicon Detectors were the size of a quarter.
Chip are microscopic patterns of semi-conductors and metals.
Print the pattern of detector you want.
  First segment into lines (most often called strips).
  Connect sensors to readout electronics (e.g. wire bonds).
  ALEPH, DELPHI, CDF, D0 were early adopters.
  Earliest implementations often provided binary (hit/no-hit) info."
CMS Silicon Strip Detectors
RMS smaller than strip pitch !!
Strip pitch 25-100 mm

## Slide 17: Double-Sided Strip Detectors
Strips provide an asymmetric resolution:
  Good:
  Bad:
Solution: Orthogonal Strips on two sides!
  Twice as many electronics channels.
  Good resolution in all directions.
  Limitation:
    Ambiguity when more than one particle per chip.
Adopted by:
  BaBar SVT
  Belle SVD
  LEP Silicon Systems
BaBar
Belle
Limited by Ambiguity!

## Slide 18: Hybrid Pixel Detectors
Question:
  If you segment a plane into pixels, How do you get the signals out.
Answer:
  Send them out of plane!
  Wafer #1 is an array of pixel sensors.
  Wafer #2 is a readout circuit (digitizes, formats, transmits data)
  An array of “soft metal bumps” is pressed to make the contacts.
    Indium, PbSn, Lead-free Solders (SnAg, SnAgCu, …)
Superb resolution!
Expensive & large material budget.
ROC is Read Out Card
ATLAS
CMS

## Slide 19: Monolithic Active Pixel Detectors (MAPS)
Hybrid Pixel Detectors are expensive and thick!
  If you only care about high momentum thickness is OK.
  If you require precision at low momentum, need a new solution.
New solution
  We have stripped & pixelized but retained a “parallel plate” field.
  Ionization electrons can be DIRECTED to a small collection point.
  In this way we create space for the readout electronics:
    Within the area of the pixel itself.
    On the SAME WAFER!
Examples:
  ALICE ITS2 (and future ITS3); sPHENIX MVTX.
ALice PIxel Detector (ALPIDE)
ALICE
sPHENIX
NOTE:
Point collection  Low Noise!

## Slide 20: Technology Overview
Silicon detectors presently provide the best position resolution.
Practical limitations ($$) most often lead to “mixed technologies”:
  Silicon pixel detectors near the collision to catch short-lived decays.
  Gas detectors at larger distance to contain costs.
Silicon Detector Evolution
Comparison to Gas Detectors

## Slide 21: ePIC Detector for EIC.
ePIC deliberately uses each tracking detector technology where it is strongest.
Near IP
Larger Radius

## Slide 22: Summary
Welcome to Nuclear Physics!!!
Detector Technology is fun and exciting.
No time for so many things readout electronics, streaming mode…
Present technology capabilities are excellent and the future is better.
You are entering nuclear physics at an amazing time.
Particularly with the future electron-ion collider.
Tomorrow we will discuss PID Technology (including one that also tracks: AC-LGAD)

## Slide 23: ePIC Detector for EIC