## Slide 1: Particle Identification Detectors
TK Hemmick

## Slide 2: How can there be more?
Calorimeters will measure energy for us.
Trackers will measure momentum for us.
So we have measured a 4-vector for every particle:
How could we possibly do better or need more than this?
Nothing is wrong per se…it is just imprecise!
  (kinda lousy at low momentum).
  (kinda lousy at high momentum).
  (kinda lousy at ALL momenta).
By the time a particle reaches detection it is ON SHELL!
  With an identified particle we can use an accurate, KNOWN MASS!
  Momentum Based: ( excellent at low momentum)
  Energy Based: (excellent at high momentum)
  Excellent measurements everywhere!
EXCELLENT!

## Slide 3: PID is really a Velocity Measurement
p = mgb E = mg velocity(b) measurement yields mass:
  Replace “Measured mass” with the known value (Particle Data Group).
  Recalculate particle 4-Vectors with improved accuracy.
  Get your physics with precision!
Today’s lecture boils down to basically goal: MEASURE b!
  Direct measurement:
    Freshman physics:
  Inference measurement:
    Velocity-dependent interactions of a charged particle with a detector!
NOTE: ePIC has made choices in PID technologies.
This presentation covers a broader scope.

## Slide 4: b Measurement Overview
Measure b Directly:
  Time-of-Flight or “TOF”
Measure b by Ionization:
  Specific Ionization (aka )
Measure b by “Optical Wake”:
  Cherenkov Radiation:
    qC measured wrt track direction.
    Thus, dependent upon deliverables from tracking
Measure b by Radiation:
  X-ray Radiation as a particle crosses index of refraction “boundaries”
  Transition Radiation Intensity
Measure b by Bremsstrahlung :
  Bremsstrahlung:
eID mechanisms
Addressed Previously by Ross Corliss

## Slide 5: Basic Concept for Time-of-Flight (TOF)
Intellectually simple.
The technology development lies in achieving excellent time resolution:
  Prompt medium response.
    e.g. Avoid scintillators doped with molecules having “delayed light”
  Quick Sensor Response
    Electrons avalanche with a “transit time”.
    Transit time “spread” degrades resolution
Collider Geometry
Rule of Thumb:
Transit time spread < Transit time.
Tiny avalanche zones have smaller TTS

## Slide 6: The “Classic” TOF: Scintillator Hodoscope
Scintillator Slat
Small PMTs with only 10 dynodes
Fast Plastic Scintillator
Smaller PMTs are usually faster because electron trajectories are shorter and more uniform. Fewer dynodes help somewhat, but the dominant factor is often the photocathode-to-first-dynode geometry. The real breakthrough in timing came from MCP-PMTs, which replaced the dynode chain entirely and reduced transit-time spreads from hundreds of picoseconds to a few tens of picoseconds.
Photomultiplier Tube (PMT)
Micro Channel Plate (MCP-PMT)
Vacuum Avalanche

## Slide 7: Fast Light Sensors for ePIC
Direct measurements of velocity require a fast charge collection device.
The time resolution is automatically helped by small devices:
  LGAD: Low Gain Avalanche Device. Instantly small.
  MCP: Micro Channel Plate  LAPPD (Large Area Picosecond Photon Detector)
Large Area Picosecond Photon Detector (LAPPD) High-Rate Picosecond Photon Detector (HRPPD)
Vacuum Avalanche

## Slide 8: Fast Timing in Gas & Silicon!
Cherenkov Light is instantaneous
CsI withstands contact with the gas
MicroMEGAS: “tiny” avalanche region.
Low Gain Avalanche Device
Silicon Avalanche
PICOSEC DETECTOR
Historically, Si not used for timing
Avalanche  large fast-rising pulse!
  Excellent timing!
These devices are BOTH trackers and TOF detectors!

## Slide 9: Ionization used for particle ID
The Bethe-Bloch formula predicts roughly that
Several effects modify this at very low and very high bg.
Fundamentally Dependent upon bg !
Particles separate into bands if plotted vs. momentum

## Slide 10: The Misery of the Landau Tail!
A Poisson Distribution gives the probability around the mean number for a series of uncorrelated events.
In the limit of high average number, it becomes Gaussian with .
One might expect that collecting a large amount of ionization leads to a precise measurement of
It’s more complicated & we must learn to deal with it.
Landau Distribution
“Long tail” Yuch!

## Slide 11: Deal with the Landau Tail!
Primary ionization e’s are produced w/ Poisson Probability
They are most often energetic enough for secondary ionization.
An unusually energetic electron is called a d-ray..
  “One lousy delta ray RUINED my whole measurement!”
Gotta learn to ignore “high ionization sample outliers”!
Dealing with the Landau Tail
High number of samples on every track:
  Fit the distribution to a Landau
Low number of samples on every track:
  “Truncated mean”
  Average the lowest xx% of samples

## Slide 12: Cluster Counting Concept
Existing Concept (using “Timepix”)
  Avalanche onto Silicon Pixels
  Tiny Pixels (smaller than cluster spacing)
  Sufficient gain for single electron
In principle can work
Expensive for large area.
Dealing with the Landau Tail
Read out a TPC with Silicon Pixels!
“Count” the primaries.
Ideally restores Poisson Statistics!
So Cool!
This is one of the very few detector concepts that attempts to defeat the Landau distribution itself.

## Slide 13: Cherenkov Light is Velocity Dependent
Cherenkov light is effectively an “Optical Boom”
  Happens when a charged particle moves through a medium faster than light.
  Example:
    In glass light travels at
    Particles in glass with generate Cherenkov light.
Photo-electron yield:
  Low index n allows for p-K separation to high momentum!
  Low index n yields very few detected photons per unit length of detector.
Cherenkov Angle determines b!
Index of refraction drives the detector design

## Slide 14: How to Determine qC
Parallel Rays converge @
The ring radius measures
Proximity Focus
qC
Snell
Cherenkov in Medium
Light follows Snell’s Law
Gap allows ring to grow.
Gap
Focus the Light
Don’t Focus
qC
Doesn't determine qc
Best used:
  Low index.
  Only e’s radiate

## Slide 15: Electron arm Proximity Focused RICH
Aerogel is extremely low-density solid.
Layer of aerogel makes Cherenkov light.
The gap between Aerogel and the HRPPD expands the ring.
Measures b by measuring qC
p
p
K

## Slide 16: Dual RICH
In the proton-going direction the hadron momenta are HIGH.
  Need a quite low index gas radiator.
To ALSO measure lower momenta, incorporate an aerogel proximity focus!
Cherenkov radiator
○ Refractive Index
n = 1.02 (aerogel) 1.0008 (C2F6)
○ Length of the radiator
L = 4 cm (aerogel) , 160 cm (C2F6)
Mirrors
Photon Detector
3 mm pixel size; 200-500 nm MAPMT
Particle Generation
Originate from the vertex

## Slide 17: Space Availability Dilemma!
The pfRICH required a ~40 cm gap to expand the ring.
The Dual RICH required a 1.6 meter gas radiator to reach to high momentum.
The barrel only has a few cm room for PID!
Calculate the index of refraction for the threshold of Total Internal Reflection
b~1
Low index; Low qc; light exits face
High index; Large qc; light exits end

## Slide 18
Detection of Internally Reflected Cherenkov: DIRC
18
:
hpDIRC
At normal incidence, Cerenkov light is internally reflected for
Cerenkov angle preserved if bars meticulously flat with 90 degree corners.
  If you “back up the photon sensors” this is a proximity focus. (original BaBar)
  If you use focusing elements it becomes a high performance hpDIRC
Spectacularly compact PID device with photon detection at end.

## Slide 19: eID by Transition Radiation (TRD)
“Threshold detector” (TR X-rays produced or not)
Pmin ~ 1 GeV (rejection ~constant at higher momentum)
1: Make TR photons:
Index, n, change
X-ray regime
Film, foam, fleece
2: Layered to get more photons
3: ID TR photons by energy/pos
4: Reject Pions
Balance between X0 and rejection

## Slide 20: Summary
Particle ID will be a critical requirement in ePIC.
No one technique can span the full range of momenta of particles produced at EIC.
When PID is critical, a suite of detector technologies must be applied.
If we have met our goal, you should be able to look at the diagram of ePIC:
  Understand the role of each detector system.
  Understand why the layer order is correct.
  Understand how the chosen technology of each system matches the physics.
PID Performance vs Momentum