## Slide 1: Hadron Storage Ring Systems
EPIOS meeting
Mar 19 – 20, 2026
Stony Brook University/Online (https://indico.cfnssbu.physics.sunysb.edu/event/648/)
Chuyu Liu
Collider-Accelerator Department, BNL

## Slide 2: Outline
RHIC Facility Overview
EIC Hadron Storage Ring
  Flat-beam
  Radial Shift
  Transition Crossing
EIC HSR Systems
  Straight Sections
  Injection System
  RF
  Hadron Cooling
  Vacuum
  Machine Protection
Summary

## Slide 3: Aerial view of the RHIC facility
NSRL
LINAC
AGS
Tandem
6:00 o’clock
8:00 o’clock
10:00 o’clock
12:00 o’clock
RHIC
4:00 o’clock
2:00 o’clock
EBISBooster
Notes: Several decades following Rutherford's landmark experiment, our understanding solidified, revealing that atoms are composed of nucleons and electrons. Furthermore, the discovery of quarks and gluons as the constituents of nucleons further expanded our knowledge. However, physicists sought to generate an abundant supply of quarks and gluons to comprehensively study their properties and interactions.

## Slide 4: Hadron Pre-injector at BNL
Linac (1970) EBIS injector (2010) Tandem (1970)
Ion: H-, H-^ H-U H-U
E: 10 -200 MeV 2 MeV/u 14 MV(1+q)
Iave : 200uA, ~150 nA ~10 μA
RR: 10 Hz 5 Hz dc/pulsed
User: BLIP, NSRL, NSRL, RHIC SEU, NSRL
RHIC RHIC,
Can serve all users simultaneously
Courtesy of Deepak Raparia

## Slide 5: Requirements for Hadron Injectors
Parameter/Species | p | Unpolarized d | He | Au | Ag
Charge number Z | 1 | 1 | 2 | 79 | 47
Mass number A | 1 | 2 | 3 | 197 | 109
Injection energy [GeV] | 23.8 | 12.2 | 11.1 | 9.8 | 10.53
Beam rigidity [T∙m] | 79.3 | 81.2 | 55.3 | 81.2 | 81.1
Bunch intensity [1010] | 32 | 15 | 13 | 0.23 | 0.39
RMS normalized emittance, h/v [mm] | 2.5 | 1.5 | 1.5 | 1.5 | 1.5
RMS longitudinal emittance [10-3 eV∙s] | 42 | 42 | 42 | 42 | 42
Polarization [%] | 75 | - | 75 | - | -
Table 1 lists the beam species and their parameters expected to be needed in the first few years of the EIC physics program. All parameters are specified at AGS extraction. Most requirement parameters are driven by the EIC physics goals including polarization and luminosity. Others are consistent with what have been demonstrated by the HIC during RHIC operation.

## Slide 6: Additional developments in the injectors
ANL (MEP Group), with University of Kentucky, is developing polarized Li-6 and Li-7 sources
  Early-stage effort
  Would expand available polarized species for EIC
  Can be installed at EBIS
A promising option for polarized deuterons:
  Use existing COSY polarized source at BNL Tandem
Ongoing development of polarized ³He in the Hadron Injector Complex

## Slide 7: Polarized 3He at the Hadron Injector Complex
Development plan:
2026-2027:Design, install & commission a polarimeter for Booster.
2027-2028: Commission polarized 3He in the Booster up to and study up to .
  Optimize and study the dynamics of the imperfection resonances.
  Study crossing the two intrinsic resonances above .
2029-2030: Commission polarized 3He in the AGS up to .
  Optimize early portion of ramp below
  Study polarization transmission in the spin-tune gap as a function of .
  Study transmission across the .
  Make determination for high energy BtA upgrade and determine need for upgrades.
Investigating potential upgrades
Booster to AGS transfer line energy upgrade to support .
An additional cold snake for crossing the resonance.
Booster corrector upgrades for generation of an appreciable spin-tune gap.
Courtesy of K. Hock

## Slide 8: EIC Hadron Storage Ring

## Slide 9: Electron-Ion Collider
Hadron Storage Ring (HSR) 10-275 GeV
  Superconducting magnets (existing)
  1160 bunches, 1A beam current (3x RHIC)
  Flat beam (11:1 ratio)
  Beam cooling
Electron Storage Ring (ESR) 5–18 GeV
  large beam current, 2.5 A  9 MW S.R. power
  S.C. RF cavities
  Need to inject polarized bunches
Electron Rapid Cycling Synchrotron (RCS) 750 MeV- 18GeV
  1 Hz
  Spin transparent due to high periodicity
Electron Injector
  Warm Linac, 30 Hz
  Beam Accumulation Ring, 1 Hz

## Slide 10: HSR Machine
Design is based on the existing RHIC Complex in BNL.
HSR will be composed of Yellow ring only and new IR6.
41 GeV bypass will be added between IR12 and IR2.
HSR warm injection line bring beams from AGS to HSR IR4, where the septum and injection kickers are located.
Low Energy Cooler is located at IR2.

## Slide 11
Key upgrades to achieve higher energy, higher current, high polarization, more bunches...
Hadron beams include:
  Polarized protons
  Polarized 3He ions
  Unpolarized ion species up to Uranium
At injection, a fully configurable bunch-by-bunch spin pattern is available for experiments.
RHIC:111 bunches all times
HSR: 290 bunches at injection
105 ns
40ns
HSR Machine (cont'd)
10ns
HSR: 1160 bunches at store

## Slide 12: Flat Beam Acceleration Beam Experiment
12
Maximum transverse beam emittance ratio 13:1 was obtained with stochastic cooling at 31 GeV/nucleon
Transverse emittance ratio 11:1 was well maintained during acceleration from 31 GeV/nucleon to 100 GeV/nucleon
Flat beam was kept at 100 GeV with EIC/HSR tunes for ~2 hours, 11:1 emittance ratio was well maintained too
Emittance Ratio
Emittance Ratio
Horizontal Emittance
Vertical Emittance
Emittance ratio
100GeV
31 GeV
Emittance ratio
Horizontal Emittance
Vertical Emittance
During Acceleration
Whole Fill
Acceleration

## Slide 13: Radial Shift Implementation
To synchronize hadron-electron revolution frequencies the radial shift is employed in the hadron ring
Beam will be switched to one inner arc for 41 GeV operation.
Radial shift implementation in RHIC was successful – see G. Robert-Demolaize et al, https://doi.org/10.1016/j.nima.2024.170043
Radial shift implementation has been established in all IR sections, except IR6
Requires upgrade of several dipole corrector power supplies in IR straights, as well as adding shunt PSs for D6 dipole magnets. The D6 have leads available (not used in RHIC).
20 mm
275 GeV
100 GeV
store

## Slide 14: Beam Energy and Average Orbit Radius in the HSR
Since the electron revolution frequency is fixed, the hadron orbit must be adjusted with energy to keep the collisions in sync.
70 mm beam pipe
20 mm
275 GeV
100 GeV
store
130 GeV
Courtesy of V. Ptitsyn

## Slide 15: Transition crossing beam study
Purpose Study transition crossing in the EIC HSR by reducing the number of active jump quadrupoles during the transition.
Goal Achieve stable transition crossing with minimal emittance growth and beam loss using fewer quadrupoles.
Results
  Initial attempts showed issues due to tune feedback oscillations
  With tune feedback off, transition crossing was successful
  No emittance blowup at 1.5×10⁹ per bunch (111 bunches)
  In a second session, all goals were achieved within 8 ramps
Conclusion
  Results suggest fewer jump quadrupoles may be feasible
  However, due to different HSR optics and layout, all 48 quadrupoles are still required

## Slide 16: Beam study observations
111 bunches, 2.2 x109 at injection
Without feedback
  No significant beam loss (~6%)
  No emittance blowup
  No clear chromatic effects
Losses are tunable
  Tune
  Chromaticity
Courtesy of H. Lovelace

## Slide 17: EIC HSR Systems

## Slide 18: HSR Straight Section Modifications
Reconfigure Yellow into HSR:
  Replace DX and D0 magnets with NC dipoles
  Redesign the warm to cold transition
  In IR10 and IR4, remove the Blue triplet and repackage Yellow triplet into smaller cryostat to provide more space in those areas
D0
Q3
DX
Q2
Q1
D0
Q3
Q2
Q1
NC Dipoles
Q3
Q2
Q1
D0
Q3
Q2
Q1
DX
D0
Q3
Q2
Q1
Q3
Q2
Q1
NC Dipoles
RHIC
HSR
IR12 triplets
IR10 triplets
IR2 triplets
IR8 triplets
IR4 triplets
18

## Slide 19: Lattice Design of Straight Sections
Beam sizes in the triplets are among the largest in the HSR.
Aperture is more of a concern at injection energy due to adiabatic damping.
The horizontal half aperture > 7*sigma_x, and the vertical half aperture > 6*sigma_y.
The lattice design informs the aperture design, and the aperture design, in turn, provides feedback to the lattice design — it’s a two-way process.
Lattice design of a typical IR, including IR8, 10, 12, 2

## Slide 20: HSR injection system
Injection system requires fast kickers due to reduced bunch spacing
Bunch spacing: 105 ns → 40.5 ns
Stripline kickers selected
Injection located at IR4 due to space constraints

## Slide 21: HSR injection system (cont’d)
Three main components:
  Warm transfer line (upstream match → periodic cells → downstream match)
  Septa: 2 DC + 1 AC (induction)
  19–20 stripline kicker modules
Key parameters:
  DC septum width: 14 mm
  AC septum width: 4 mm
Kicker requirement:
  Provide sufficient separation between injected and circulating beams
  Avoid beam scraping
  Required kick angle: 0.7 mrad

## Slide 22: HSR Transfer Line
New warm transfer line extends the existing ATR line to IR4
Reuses combined-function magnets from the RHIC Blue transfer line
New quadrupoles (APS design can be used)
Matching:
Upstream
Periodic Cells
Downstream
AGS to HSR transfer line

## Slide 23: The Life Cycle of Hadron Beam
tuning
injection
ramp
store
Bunch split
Bunch compression
Radial shift
Crab cavity on
Bunch profile evolution
Current (A)
Bunch length (ns)
5 nC
44 nC
Au transition crossing

## Slide 24: ASR NCRF Systems
4x 24.6 MHz NCRF Cavities
  Capture and acceleration, repurpose from RHIC 28 MHz cavities
3x 49 MHz NCRF Cavities
  290 to 580 Bunch splitting, new cavities
4x 98 MHz NCRF Cavities
  580 to 1160 Bunch splitting, new cavities
8x 197 MHz NCRF Cavities
  Bunch compression (together with 591 MHz SRF cavities), repurpose from RHIC 197 MHz cavities
Courtesy of Binping Xiao

## Slide 25: Hadron Cooling in the EIC
Protons and ions will be precooled at 24 GeV using Electron Cooling.
Heavy ions at collision energies will be cooled using Stochastic Cooling.
Currently, no hadron cooling of proton is implemented at collision energies. However, it may be added in the future to increase the EIC average luminosity during store.

## Slide 26
DC Gun
400kV
e-
Laser
197 MHz
930 kW Beam Dump
16x 197 MHz
NCRF LINAC
extraction
injection
cooling
HSR
4x 591 MHz
NCRF correction Cavities
180° Dipole
Spectrometer
Quad
Cathode transport
Mu-metal shielding
24MHz
RF cavity
SC Quad
130 kW Beam Dump
Extraction line
Injector/linac
Test line
Solenoids
LEReC Cooling Solenoids
180°Dipole
(U-turn)
transport
PM
PM
PM
RF diagnostics line with Deflecting cavity
Injector test
e-
HSR
hadron
hadron
hadron
e-
RF diagnostic
Not to scale
Low-Energy Cooler (LEC) for the EIC
The LEC is scaled up version of LEReC (which operated 2019-2025):
more RF cavities, longer cooling section, higher beam current.
Courtesy of Alexei Fedotov

## Slide 27: HSR Existing Vacuum System
Existing cold bore beam pipes are stainless steel
  High surface resistance -> Excessive resistive wall heating
  High secondary electron yield (SEY) -> Electron cloud formation
Aggressive new parameters required for EIC
  High stored current (.72 A vs .27 A)
  Reduced bunch length (60 cm vs 600 cm)
  Short bunch spacing (10 ns vs 108 ns)
  High bunch charge (1.2x1011 ppb)

## Slide 28: Resistive wall
Stainless-steel
beam pipe
Resistive Wall Heating and Mitigation
Proton beam induces ~2.5 W/m heat load on existing stainless-steel beam pipe
RHIC triplets have limited cooling capacity, reducing thermal margin
This increases the risk of magnet quench
Solution
Install a beam screen with high-conductivity surface
Use high-RRR (≥50) copper to reduce resistive heating
112.75 mm
Beampipe
w Beam Screen

## Slide 29: Electron cloud predictions
[Xiaofeng Gu]
Electron cloud simulations (PyECLOUD) show buildup when SEY ≥ 1.20.
Amorphous carbon has low SEY by default and does not require activation or conditioning, unlike NEG or TiN.

## Slide 30: Magnet Interconnect Assembly
Extraction bushing
Helium jumper line
Anti-rotation extraction flange
Fixed extraction flange
Interconnect module
Extraction bushing
Strain relief bracket
Existing magnet cold bore
Thermal strap
Beam position monitor
Existing magnet cold bore
Flexible RF bridge
Gold plated contact ring
Spring ring
Pumping slots
Courtesy of Charlie Hetzel

## Slide 31: HSR Collimation & Losses
Preliminary results:
  Collimation inefficiency < 10−5 [m−1] (≈LHC-level) → beam losses escaped collimators and reached IR6
  Beam lifetime (IBS, beam-beam, Touschek) at 6σ aperture is > 7 hours → 60 pb−1 per 10 hrs. fill
  The heat load in cold sections is below the limit (~0.5 mW/m)
  No losses in the ePIC region
  Setup simulations for BFPP gold ions () → one of the major damage sources at LHC experiments
Tool: Xsuite
Method: Annular halo for betatron and RF sweep for momentum collimation (CERN-like)
Setup: One primary with two secondary betatron per plane + one primary with two secondary momentum
  → 9 collimators in IR12
  + 2 vertical tertiary collimators in IR8
IR6-FWD
IR4
IR2
IR12
IR10
IR8
IR6-BWD
Power [W/m]
104
102
10−6
10−4
10−2
1
Power [W/m]
104
102
10−6
10−4
10−2
1
0
1000
2000
3000
4000
S [m]
Proton 275 GeV
Au ions 110 AGeV
HSR
Courtesy of Andrii Natochii

## Slide 32
Secondary mom. H-coll.
HSR Collimators in IR12
End Cold Section
End Cold Section
HSR
ESR
Secondary H-coll.
Secondary H-coll.
Primary H-coll.
Primary V-coll.
Secondary V-coll.
Secondary V-coll.
Secondary mom. H-coll.
Primary mom. H-coll.
Courtesy of Andrii Natochii

## Slide 33: RHIC/HSR dump kickers parameters
From RHIC Configuration Manual
Courtesy of A. Drees
Courtesy of E. Skordis

## Slide 34: HSR Proton beam dump temperatures 4/5 kickers
Dumped Beam
Circulating Beam
Graphite
Titanium Window
Carbon Carbon
Stainless Steel
  Titanium window to surpass 600 Celsius (1.2kJ/cm3 peak)

## Slide 35: HSR Gold Ion beam dump Energy dens. 5/5 kickers
Dumped Beam
Circulating Beam

## Slide 36: Upgrades to the HSR abort system
Issue #1: kicker pre-fire, potential damage of machine and detector components. Solution: change from Thyratron tube to solid state switches
Issue #2: coupling impedance due to in-vacuum kicker magnet. Solution: redesign kicker magnets with coated ceramic beam pipe.
Issue #3: overheating of beam dump due to flat beam. Solution: add a vertical kicker magnet to disperse flat beam.
LHC MKD as a model

## Slide 37: Summary
Injector complex will be ready to support operations Ensures reliable beam delivery for commissioning and physics
Built on RHIC with targeted upgrades Including but not limited to the injection, RF, straight sections, vacuum, and machine protection systems
Key performance features validated Flat-beam acceleration, radial shift, and transition crossing with missing quads demonstrated in RHIC
On track toward CD-2 Steady progress within the ASR subproject

## Slide 38: Additional slides

## Slide 39: Energy and average orbit radius for different ion species at RHIC maximum beam rigidity (833 T*m)
U
Au
Zr
Ru
Cu
d
3He
p

## Slide 40: Beam Screens
Design based on the LHC beam screen
Copper cladded stainless steel
  P506 stainless, C10100 OFE copper
Operating temperature: 4.5-10K
  Single cooling tube (no synchrotron radiation)
Beam facing surfaces require aC coating
Cooling tube (8mm)
Cooling tube support
Copper cladded SS
Beam screen guide
Cooling tube laser welded
Beam screen prototype
Courtesy of Charlie Hetzel

## Slide 41: aC Coating
Proof of principle coating system
  Cycle time meets production requirements
Clean tent area for production complete (40x100’ [12.2x30.5m])
Full length (36’ [11m]) engineering validation system completed
  Preparing for first coating run
Ultrasonic cleaning equipment (36’ [11m]) commissioned
Cleaning facility
Coating Facility
Graphite target inside beam screen
POP horizontal coating system

## Slide 42: Proposal for EIC Science Program in the First Years
Year - 1
Start EIC Science
New Capability:
Commission electron polarization in parallel
Collider:
10 GeV electrons on 115 GeV/u heavy ion beams (Ag or Nb)
Year - 2
+Long. electron polarization
New Capability:
Commission proton polarization in parallel
Collider (base goal):
10 GeV long. polarized electrons on 130 GeV/u Deuterium
Collider (stretch goal):
Last weeks: 10 GeV long. polarized electrons and 130 GeV polarized protons
Year - 3
+Long. electron polarization
+ Proton polarization
New Capability:
Commission hadron spin rotators
Collider (base goal):
10 GeV long. polarized electrons on 130 GeV transverse-polarized protons
Collider (stretch goal):
Last weeks switch to longitudinal proton polarization
Year - 4
+ Long. electron polarization
+ Proton polarization
+ Hadron spin rotators
New Capability:
Commission hadron accelerator to operate with off-center orbits
Collider (base goal):
10 GeV long. polarized electrons on 100 GeV Au
Collider (stretch goal):
10 GeV long. polarized electrons on 250 GeV transverse and longitudinal polarized protons
Year - 5
+ Long. electron polarization
+ Proton polarization
+ Hadron spin rotators
+ Hadron beams with off-center orbits
Collider (base goal):
10 GeV long. polarized electrons on 100 GeV Au
Collider (stretch goal):
10 GeV long. polarized electrons on 166 GeV transverse and longitudinal polarized He-3
Time to construct the ELR subproject