## Slide 1: AI/ML in Polarized Beams and Sources
20 March 2026 2026 EPIOS Meeting
Kevin Brown, for the EIC-BeamAI Collaboration
C-A Dept., Brookhaven National Laboratory &
ECE Dept., Stony Brook University
With help from:
Antonino Cannavo (OPPIS) and Noah B. Wuerfel (He3 Ion Source)

## Slide 2: Outline
Current activities:
  Overview of AI/ML funded projects to date
  NARAD project
Polarization improvements with AI/ML projects
Issues in preparing for EIC
  Longitudinal emittance
  Transverse emittance
  Optics measurements and ORM analysis
AI/ML in Ion Sources
Summary
List of publications (including submitted or in-progress) and Presentations

## Slide 3: Overview of AI/ML funded projects to date
Higher RHIC polarization by Physics-informed Bayesian Learning
  NP funded, $1.5M, duration 2 years, start 09/01/2023
  BNL, Cornell, JLAB, SLAC, RPI
  Plans presented in 2023 C-AD MAC
Toward higher brightness and polarization of hadron beams: Digital-Twin-based autonomous control of BNL’s hadron accelerator chain
  NP funded, $1.5M, 2 years, continuation/renewal
  BNL, Cornell, JLAB, SLAC, FNAL, RPI
Developing AI-Ready Data Framework for DOE NP Particle Accelerators
  Now called NARAD = NP AI-Ready Accelerator Data
  ASCR/NP funded, $4M, duration 2 years, start 10/1/2025
  JLAB (lead), BNL, Cornell, LBNL, PNNL (+ informally, FNAL and SLAC)
Additional collaborations
Particle Accelerator Lattice Standard (PALS)
python Accelerator Middle Layer (pyAML)
Multi-Office particle Accelerator Team (MOAT)

## Slide 4
Machine Learning for Accelerator Operations
Goal: Improve beam quality and operational efficiency.
Automated beam tuning
Operational Digital Twin
Data-driven model calibration
Fast adaptive control
Case studies: BNL hadron injector complex

## Slide 5: NP AI-Ready Accelerator Data (NARAD)
Local Machine
Description
PALS
Description
American Science
Cloud, Foundation
Models, AI systems,
ModCon

## Slide 6: NP AI-Ready Accelerator Data (NARAD)
Goal: Create an AI-ready, standardized accelerator data + lattice representation (PALS) and develop facility-agnostic modeling and optimization workflow.

## Slide 7: Polarization Performance
 | Max Energy [GeV] | Pol. At Max Energy [%] | Polarimeter
Source+Linac | 1.1 | 82-84 | 
Booster | 2.5 | ~80-84 | 
AGS | 23.8 | 67-70 | p-Carbon
RHIC | 255 | 55-60 | Jet, full store avg*
 | Relative Ramp Polarization Loss (Run 17, full run avg)
AGS | 17 %
RHIC | 8 %
Tandem van de Graaff
Polarimetry available at:
Source
End of Linac (200 MeV)
AGS extraction
RHIC injection energy
RHIC flattop
(No Booster polarimeter!)s
From Vincent Schoefer 2023 talk.

## Slide 8: High polarization through brighter beams and AI enabled corrections
Making polarization measurements is slow, so we instead focus on indirect measurements to optimize polarization
  Make smaller emittance, brighter beams
  Reduce coupling to minimize vertical emittance
  Reduce space charge blow-up
  Automate to maintain optimum states
  Improved physics models to better inform improvements. Provide virtual diagnostics
  Improve existing diagnostics
The line is not a fit.

## Slide 9: Ongoing and Planned efforts
Coupling correction in LtB
Long term optimization (perhaps with RL or via Digital twin) of LtB and Booster Injection
Optimization of AGS injection
Reducing space charge driven emittance growth in AGS
Developing better emittance monitors in injectors
Digital twin of AGS to support skew quad spin correction
AI/ML tool for Booster and AGS energy (calibrating Gg meters)
Long term – digital twins of Booster and AGS
Question: can the new Booster polarimeter be used/adapted to measure emittance?

## Slide 10: Coupling measurement in LtB
H- beam is born inside a solenoid in OPPIS as transversely coupled beam
Multiple quadrupole scans have been performed at various locations of the LtB beam line, while changing the solenoid strength
Data analysis and simulation studies to quantify coupling is in progress

## Slide 11
AGS Bunch Merging Optimization with RL
Goal: Obtain a good merged bunch profile – low emittance growth, no loss, centered and stable.
RL Optimization
RL agent trained to minimize emittance growth.
Begins from poor merge conditions; finds good RF settings after one step.
Comparable performance to operational settings.
LLM-based policy teacher for RL agent in development, leads to faster convergence and better performance.
Initial bad merge
RL optimized merge

## Slide 12
Anomalous
Normal
Classifier predictions on archive data
Improving AGS IPM Emittance Measurement with ML
Goal: Improve emittance reconstruction accuracy and robustness of AGS Ion Profile Monitor.
Simulated scan with surface fitting
Approach
Gaussian process based surrogate model for fast IPM profile inference.
Unsupervised anomaly classifier to detect atypical IPM profiles.
Outcome
Improved accuracy in reconstructed bunch size and automated detection of anomalous IPM signals.

## Slide 13: Injection Optimization with BO
LtB Injection Optimization
BO maximizes Booster beam intensity using LtB optics.
Beam size decrease in both planes during LtB optimization.
BtA Injection Optimization
BO maximizes beam transmission efficiency using using BtA optics.
20% improvement from operational settings.

## Slide 14: Uncertainty Quantification to Improve Booster Model
Goal: Use Bayesian Uncertainty Quantification (UQ) to characterize and reduce model-data mismatches, assisting Digital Twin development.
Approach
Bayesian UQ analyzes orbit response discrepancies.
Neural Network surrogate model accelerates UQ process.
Outcome
UQ analysis investigates quadrupole field errors as possible sources of errors.
Incorporating UQ results improves agreement between simulation and measurement.

## Slide 15: AI/ML in Ion Sources
OPPIS
  Optimize tuning from Tank 9 to Polarimeter
  Optimize LEBT beam tune
  Rb cell design
He3 Source
  Optimize polarization from RFQ to polarimeter
  AI/ML enhanced modeling of ionization in EBIS
  Design of RF electrodes and cell shapes
  Dynamic plasma tuning

## Slide 16: Optically Pumped Polarized Ion Source
to LEBT
OPPIS produces 3-5 mA Polarized H- ion pulse current
81-84% polarization @200 MeV , 0.5 mA
D. Raparia 25/06/18
Notes: General Introduction of the OPPIS source.
All three main blocks of the OPPIS were developed with either minor or major upgrades

## Slide 17: 1 – Beam tuning from tank 9 to the 200 MeV polarimeter
Beam Optics element to be tuned
Beam Loss Monitor
Detectors signals at polarimeter
Beam profile MultiWire detector

## Slide 18
- Beam tuning LEBT
- Separation between residual unpolarized 39 keV and polarized beam 35 keV after BM1
Source and Beam Optics element to be tuned
Scintillator image of beams after dipole magnet BM1
Beam Current profiles after dipole magnet BM1
2

## Slide 19: 3 – Drive the design of the Rb cell based on optimized physical models
Gap width
Gap width
OPTICAL PUMPING
Laser Absorption
Depolarizing collisions:
  Rb + Rb
  Rb + wall
Radiation trapping
p + Rb INTERACTION
- Neutralization Probability
Competing reactions?
  Elastic scattering
  Ionization ,
  Residual gas

## Slide 20
He3 Beamline Polarization optimization from RFQ to Absolute polarimeter
Tune many beamline elements after EBIS LEBT to minimize polarization loses to Booster.
Dynamic spin tune maintenance.
Model of chicane before Booster with line to absolute 3He nuclear polarimeter

## Slide 24: Summary
Connection to EIC and DOE AI missions
Genesis Mission building a unified AI platform for accelerator science
Injector ML experience enables AI-assisted operation for EIC
NARAD developing cross-facility AI-ready workflow
Injector and source ML incorporation
Automated beam-tuning routines
Experiments show we can reduce emittances by 20%. 4 times faster than an operator.
Operational bidirectional Digital Twin
Streamlined model calibration
Bunch merging to suppress space charge driven growth reduced transverse emittance by 15%.
A well-trained RL model makes the correction in just a handful of steps.
Robust anomaly detection and diagnostics
Optimization through design
Community & infrastructure efforts
DOE-funded projects and collaborations: NARAD, MOAT, AmSC, EIC-BeamAI

## Slide 25: Acknowledgment
Kevin Brown, Yuan Gao, Eiad Hamwi, Levente Hajdu, Christopher Kelly, Trevor Olsen, Vincent Schoefer, Nathan Urban
Georg Hoffstaetter de Torquat, David Sagan
Auralee Edelen, Ryan Roussel
Armen Kasparian, Kishansingh Rajput, Todd Satogata
Yinan Wang, Yue Zhao
Christopher Hall
Tia Miceli
Work supported by Brookhaven Science Associates, LLC under Contract No. DE-SC0012704 and No. DE-SC0024287 with the U.S. Department of Energy and by NASA (Contract No. T570X).

## Slide 26: Publications
[1] Y. Gao et al., “Applying Bayesian Optimization to Achieve Optimum Cooling at the Low Energy RHIC Electron Cooling System”, Physical Review Accelerators and Beams 25, 014601 (2022).
[2] W. Lin et al., “Simulation Studies and Machine Learning Applications at the Coherent electron Cooling experiment at RHIC”, in Proc. IPAC'22, Bangkok, Thailand, Jun. 2022, pp. 2387-2390.
[3] W. Lin et al., “Machine learning applications for orbit and optics correction at the Alternating Gradient Synchrotron”, in Proc. IPAC'23, Venice, Italy, May 2023, pp. 4460-4463.
[4] W. Lin et al., “AGS Booster model calibration and digital-twin development”, in Proc. IPAC’24, Nashville, TN, May 2024, pp. 3449-3452.
[5] R. Roussel et al., “Bayesian Optimization Algorithms for Accelerator Physics”, Physical Review Accelerators and Beams 27, 084801 (2024).
[6] T. Balasooriya et al., “Reinforcement Learning for Charged Particle Beam Control to Minimize Injection Mismatch in Particle Accelerators”, ICASSP 2025 - 2025 IEEE International Conference on Acoustics, Speech and Signal Processing (ICASSP), Hyderabad, India, 2025, pp. 1-5.
[7] W. Lin, “Maintaining optimal beam brightness and luminosity using machine learning”, in Proc. HIAT2025, East Lansing, MI, Jun. 2025, pp. 79-84.
[8] W. Lin et al., “Improve beam brightness with Bayesian optimization at the AGS Booster injection at BNL”, in Proc. NAPAC’25, Sacramento, CA, Aug. 2025, pp. 157-159.
[9] E. Hamwi et al., “Application of Bayesian optimization to BtA injection at BNL”, in Proc. NAPAC’25, Sacramento, CA, Aug. 2025, pp. 58-60.
[10] W. Lin et al., “Machine learning assisted Bayesian calibration of accelerator digital twin from orbit response data”, in Proc. NAPAC’25, Sacramento, CA, Aug. 2025, pp. 177-180.
[11] Y. Gao et al., “Exploring Reinforcement Learning for Optimal Bunch Merge in the AGS”, in New York Scientific Data Summit 2025, pp. 13-16 (2025).
[12] T. Miceli et al., “Twinac: initiation of a community-driven accelerator digital twin framework”, in Proc. ICALEPCS’25, Chicago, IL, USA, Sep. 2025, pp. 72-79.
[13] L. Hajdu et al., “Image processing with ML for automated tuning of the NASA Space Radiation Laboratory beam line”, in Proc. ICALEPCS2025, Chicago, Sep. 2025, pp. 1008-1011.
[14] W. Lin et al., “Digital twin development for the NASA space radiation laboratory”, submitted to Physical Review Accelerators and Beams, Nov. 2025.

## Slide 27: Presentations / Talks
[1] A. Edelen, “Physics Informed and Bayesian Machine Learning for Maximization of Beam Polarization at RHIC”, presentation at the 4th ICFA Beam Dynamics Mini-Workshop on Machine Learning Applications for Particle Accelerators (MaLAPA 2024), Gyeongju, South Korea, March 5, 2024.
[2] W. Lin, “Maintaining optimal beam brightness and luminosity using machine learning”, presentation at the 16th International Conference on Heavy Ion Accelerator Technology (HIAT 2025), East Lansing, MI, USA, June 24, 2025.
[3] W. Lin, “Extraction bump digital twin for NSRL slow extraction”, presentation at the 6th Slow Extraction Workshop (SX 2025), Stony Brook, NY, USA, October 8, 2025.
[3] E. Hamwi, “Use of AI/ML for higher brightness and higher polarization of hadron beams”, presentation at the Artificial Intelligence for the Electron Ion Collider (AI4EIC 2025), Boston, MA, USA, October 27, 2025.
[4] C. Kelly, “Machine-Learning–Accelerated Bayesian Uncertainty Quantification for Digital Twin Modeling and Control of the AGS Booster”, presentation at the Artificial Intelligence for the Electron Ion Collider (AI4EIC 2025), Boston, MA, USA, October 27, 2025.
[5] C. Hall, “Machine Learning Approaches to Improve Ion Profile Monitor Measurements”, presentation at the Artificial Intelligence for the Electron Ion Collider (AI4EIC 2025), Boston, MA, USA, October 27, 2025.